## Slide 1: Basic Telecom – Ice Breaker

## Slide 2: Objectives
At the end of this session, you will be able to:
  Understand a typical composition of systems available at any TELCO operator
  Locate the context of communication network in a TELCO stack
  Understand the difference between network element, network architecture and services
  Understand yesterday’s and today’s services

## Slide 3: Agenda
TELCO Operator stack
Telecom Business
Telecom Services: Yesterday and Today
Notes: TELCO : Telecom Company

## Slide 4: What is Telecom Umbrella?
BSS
OSS
NMS
Network
Business Intelligence, Portal, CRM, Rating, Billing Payments, Debt Management, Revenue Assurance, Fraud Management, Settlements
Order Management, Provisioning, Network Inventory Management
Fault Management, Performance Management, Mediation
GSM, PSTN, Broadband, Cable, Satellite
We will concentrate on !!!

## Slide 5: Telecom Business
Service Providers
NE Suppliers
$$

## Slide 6: Services Yesterday
Connectivity Layer
End User Services
VAS
Voice
FAX
SMS

## Slide 7: Services - Today and Tomorrow
End User Services
Content & Application Layer
Video Streaming
Messaging
ERP systems
Community Portal
Commerce Apps
Mail Services
Still Imaging
VOIP
Connectivity Layer
VAS
Voice
FAX
SMS

## Slide 8: Summary
In this session, we have learned:
  Typical composition of systems available at any TELCO operator
  Context of communication network in a TELCO stack
  Difference between network element, network architecture and services
  Yesterday’s and today’s services
Notes: TELCO stands for Telecom Company

## Slide 9: Thank You

## Slide 10: PSTN: An Introduction
Notes: Let’s start with PSTN Introduction..By the way PSTN stands for Public switch telephone network

## Slide 11: Objectives
At the end of this session, you will be able to:
  Explain telecom evolution and typical milestones in telecom evaluation
  Understand typical composition of PSTN network and its topology
  Understand PSTN access network composition
  Understand basic terminologies used in PSTN network such as local loop, signaling, trunk, central office, etc.
  Understand typical scheme of PSTN addressing
  Understand signaling classification

## Slide 12: Agenda
Telecom Evolution
PSTN: Nuts and Bolts
PSTN: Typical Network Composition
Addressing and Routing
LATA, LEX and IXC
Introduction to signaling

## Slide 13: Telecommunication Evolution
Communication
Mail, etc.
Telecommunication
Telephony
Fax
Videoconference
E-mail
File Transfer
Notes: Telecommunication evolution
Meaning of Tele happens to be far , so it is far or distance communication…
Again in the today’s context there is no really no meaning for word ‘FAR’ goes. Nevertheless, I will not be surprised if communication crosses galaxies and planets in the days to come…we may find an address of website like … www.google.nr.milkiway
Shown in front are some modes of communication like Telephony, fax, video conference , email etc….
Of left side we have a typical Postal mail service …
Let’s move on further…

## Slide 14: History of Telecom: An Overview
1837: Samuel Morse invents the telegraph
1858: Transoceanic telegraph cable was laid
1876: Alexander Graham Bell invents the telephone
1877: Bell Telephone company was formed
1885: Incorporation of AT&T
1892: Invention of Strowger exchange
1912: Invention of initial crossbar exchange
1971: First electronic exchange, Fax
1976:Common Channel Signaling Introduced in Telecom Network
1980:Computer Telephony Introduced
1990:
  Digital telephony (SW/Transmission/Signaling), Video Conferencing
  Cell Phone
  Radio Paging
2000: Digital End To End service, Digital Mobile, Messaging,
80 Service,Colour fax, Video Phone etc.
Notes: Here are typical milestones achieved in the area of communication..yearwise
1837: A major break throrugh …Samuel Morse invented telegraph…prior to that communication was in very very initial stage…In this mode of communication information or data was transferred as a morse code
Year 1858.. This is the year where first ever transoceanic telegraph cable was laid
Again a major break though in year 1876: Alexander Graham Bell invented telephone
Year 1877… Bell Telephone company was formed
1885… Incorporation of AT&T
Again a very major breakthrough in 1892…Invention of Strowger exchange Because prior to that what we had was a manual exchange but credit goes to this gentleman called Strowzer who have replaced human intervention and invented first ever automatic exchange that is why the name Strowzer exchange
Year 1912: Limitations of Strowzer exchange lead to an Invention of initial crossbar exchange
And finally year 1971 where First electronic exchange was developed….

## Slide 15: PSTN Characteristics
Public Switched Telephone Network
  Consists of transmission paths and nodes
  Based on star or mesh topologies, but made hierarchical across countries.
  Originally designed to carry voice but being used to carry data also
  Analog access , 300 Hz to 3400 Hz from Subscriber end, digital bandwidth 64 Kbps from exchange side (Extended to subscriber in ISDN).
  Circuit switched duplex connection
Notes: Let’s have a look at more details and the characteristics of PSTN
PSTN – Public Switch Telephone Network
PSTN consists of transmission paths and nodes
It is based on star or mesh topologies. By the way, topology is nothing but physical layout of the network. Telephones are connected to local exchange in a star topology and exchanges are connected with each other in a hierarchical mesh to have a better redundancy.
Let’s move onto next point. It was originally designed to carry voice but as you know ….now a days even data also is carried through telephony network. Of course the data rate is low.
It was meant for an Analog access , in the frequency range of 300 Hz to 3400 Hz. It happens to be a human voice range. By the way, it is worth to mention here that – human being can speak in the frequency range of 300 Hz to 3400 Hz but human can listen till 20Khz. Beyond 20Khz, human ear is going to act as a filer and it will never let above frequencies go inside. Digital bandwidth of voice communication comes out to be 64 Kbps. And we will soon see as to how this figure of 64Kbps is derived.
PSTN is Circuit switched duplex connection. The meaning of circuit switching is , end to end connection or so called circuit is fist established prior to communication and the meaning of duplex connection is two way data transfer can happen. Rather PSTN is full duplex in a sense voice communication can happen both way simultaneously also.

## Slide 16: Transmission Techniques
Simplex
  In only one direction from transmitter to receiver.
  Example: radio,TV, Paging
Half-Duplex
  Two-way communications but in only one direction at a time.
  Example: walkie-talkie/Police wireless
Full-Duplex
  Simultaneous two-way communications
  Example: PSTN, Videoconferencing, Mobile cellular
Notes: Let’s try n understand different transmission techniques…
Simplex Communication: here direction of communication is only one way i.e. from transmitter to receiver. And the examples of simplex communication are : Radio , TV, Keyboard and display. For example, we can only take input from a keyboard, we can not output to a keyboard. Similarly we can only output to a console or a display device and the radio and TV transmission are the systems where we have radio transmitter or a TV transmitter which will transmit the signal and what we have , at our homes or business houses , are radio or TV receivers. And that is precisely we call radio and TV as a receiver.
Let’s go to next technique.
Half duplex communication …In this category, communication can happen in both the directions but not simultaneously…Example is walkie-talkie
On the contrary , Full-Duplex communication happens in both directions simultaneously. This is a difference between a half duplex and full duplex communication. Examples of full duplex communication are videoconferencing , telephony , computer network. In telephony both party can talk simultaneously…it is a different story that we as a human being never do so because communication path being used is same and the kios may occur so we follow a half duplex communication

## Slide 17: PSTN – Nuts and Bolts
CPE: Customer Premises Equipment (telephone & interfaces)
Transmission Medium
Switching Nodes
  Switching nodes which will establish a communication between end subscribers on demand
Signaling Systems
1 Mm
300 Hz
10 km
30 kHz
100 m
3 MHz
1 m
300 MHz
10 mm
30 GHz
100 m
3 THz
1 m
300 THz
visible light
VLF
LF
MF
HF
VHF
UHF
SHF
EHF
infrared
UV
optical transmission
coax cable
twisted pair
Notes: Here are nuts and bolts of PSTN. A composition of PSTN…
Customer Premises Equipment , Transmission medium and the switching nodes…
Let’s begin with CPE…As the name indicates it is the equipment that is installed by the service provider on a request by a customer at the customer premises.
Next thing is the transmission medium…
=============================
PSTN network is composed of CPE Customer Premise Equipment so called telephone, switching nodes or exchanges and transmission media to interconnection exchanges.
Communication media can be classified as wireline and wireless. Under wireline category , we have copper wire which comes in two forms – co-axial cable used for cabel TV and CN and twisted pair used for CN , Telephony. On the other hand we have fiber cable which can be throught of FAT wire. Fat in terms of bandwidth and amount information carrying capacity. By the way , nature of signal gets transmitted through fiber is light.
Under wireless category we have AIR. Electromagnetic waves of different frequency ranging from low to very high traverse through air. Even though AIR through with EM waves are transmitted is free and non propriatary , the freq. bands are licensed.
.
VLF = Very Low Frequency LF = Low Frequency (Submarine) MF = Medium Frequency (AM)
HF = High Frequency (AM) VHF = Very High Frequency (TV, Mobile)
UHF = Ultra High Frequency (TV, Mobile) SHF = Super High Frequency (Satellite)
EHF = Extra High Frequency(Satellite) OPTICAL = Optical Fiber links (IR)
UV = Ultraviolet Light
Nodes : Switches has gone a revolution starting from Manual switching, mechanical switching , electromechanical switching to today’s automatic switching
Types :
Local switch
Transit switch
International switch

## Slide 18: Telephone Network at an Abstract Level
ACCESS
CORE
Access Networks: The portion of public switched network that connects access node (edge of access n/w) to the individual subscriber
Core Network: Combination of switching centers and transmission systems connecting switching centers.
Notes: PSTN is a combination of core network and access networks.
Core Network:
Combination of switching centers and transmission systems connecting switching centers. Switches are arranged in hierarchical meshy way. Transmission medium used in Fiber optic or air to send micro waves.
Access Network is the portion of public switched network that connects access node (edge of access n/w) to the individual subscriber
Access network in world is predominantly twisted copper wire connected to Analog telephone.

## Slide 19: Access Network: Wireline Local Loop
Pillar
MDF
Distribution Point
Wall Socket
Wall Socket
Distribution Point
Local
Exchange
Notes: This is how a typical access network composition will look like. What you see over here is a wireline access network. Here every where in the access network there is wire. By the way in case of PSTN, access network uses twisted pair wire.
Let’s begin a journey from Customer premises equipment or so called telephone. Telephone of connected to wall socket. Wall socket is connection to distribution point which is typically a red box or a blue box. It is basically a passive concentration point. From Distribution point connections are brought onto a pillar and from Pillar multiple such connections are brought and terminated at MDF situated in the local exchange. By the MDF stands for Main Distribution Frame. Behind MDF, there is LIC card which will take care of A-2-D and D-2-A conversion i.e. analog to digital and digital to analog conversion in case of digital exchange.
=======
Let’s have a look some terminology with reference to access network.
Local Loop :
The local loop is the telephone line that runs from the telephone company’s local exchange to your home or business. It is also called as Subscriber local loop or In the US Telecom scenario it called as “Last Mile”. It starts with Telephone at the subscribers end which is connected to wall socket, which in turn are connected to distribution point were all line are from the wall sockets in localized area are collected . DPs are connected to Pillar which a concentration point for DPs and finally all lines from Piller are terminated at MDF i.e. Main Distribution Frame at local exchange. Transmission of voice from telephone to exchange is analog in nature. It is interesting to note that power for telephone is provided by an exchange.

## Slide 20: Access Network: Wireless [WILL]
Radio is sometimes cheaper than digging the streets!
Where wire can not reach
Notes: …this is especially a solution …. Where wire can not reach for whet ever reason and exchange has facility

## Slide 21: Topology - Star

## Slide 22: Telephone Network Topology
Mesh-shaped network with direct connections between every node
The network hierarchy according to the ITU-T
Notes: Slide added for clarity. It is repeated else where also.

## Slide 23: Introduction - Telephone Systems
Local Loop
  The pair of wires that runs from the Telephone Exchange into our home or business office
Phone Line
  Communication path between CO(central office) and our home
  Twisted pair 22 AWG or 0.5 mm copper wires
Line Circuit
  The voltage applied to the line to drive the telephone is -48 Volts DC
Central Office
  is the hub of a city’s telephone network, providing power for the telephones, routing the calls ,and recording the necessary billing information. Also known as Telephone Exchange
Trunk communication path between CO’s
Switch a device that routes communications to different parties

## Slide 24: TELCO Network – An Architecture
LEC
LEC
LEC
LEC
LEC
LEC
`
CO
6234567
6292905
6433180
4776970
6736476
CO
CO
`
RE
Notes: Local Loop
  the pair of wires that runs from the Telephone Exchange into our home or business office connecting to CPE.
Local Exchange
  is the hub for location’s telephone network
Central Office
  is the hub of a city’s telephone network, providing power for the telephones, routing the calls ,and recording the necessary billing information. Also known as Telephone Exchange. If you place a long distance call, the central office passes your telephone call off to a long distance provider.
Trunk
A trunk is a special telephone line that runs between central offices and other telephone company switching centers.
A trunk is usually digital, high speed, and carries multiple telephone circuits.
Switch
  a device that routes communications to different parties.
LATA (Local Access Transport Area ) Again in US context the area being server by local exchange is called LATA.
The USA is divided into a few hundred local access transport areas (LATAs).
LEC ( Local Exchange Carrier )
Telco operator who offers services in LATA are called Local exchange carrier. If your call stays within a LATA, it is a local distance call and is handled by a local telephone company called LEC.
IXC ( Inter Exchange Carrier )
If your call goes from one LATA to another and happens to be a long distance call and is handled by a long distance telephone company called Inter exchange carrier. MCI , Sprint , AT&T are dominant players in IXC area.
A telephone number is an unique identification of subscriber in the world. To uniquely identify one subscriber , telephone number consists of Country code , city/area code, an exchange code and a subscriber number.

## Slide 25: Addressing and Routing
Each subscriber has address (telephone number)
  Hierarchical addresses
Telephone address used for setting up route from caller to callee
091
020
253
66689
country
code
City/area
code
number of
local
exchange
subscriber
number

## Slide 26: LATA, LEC and IXC
Notes: LATA …Local Access Transport Area
LEC : Local Exchange Carrier
IXC : Interexchange Carrier
POP: Point of Presence

## Slide 27: Introduction - Voice Signaling
Signal Name
  Off-hook
  Dial tone
  Address
  Ring tone
  Busy Signal
  On-hook
  Supervision
Function
  Informs CO that user want to call
  Informs user to Dial numbers
  User Dials Number
  Informs user that destination phone is ringing
  Informs the user that destination phone is in use
  Informs CO that user has disconnected
  Supervises the condition of subscriber state

## Slide 28: Summary
In this session, we have learned:
  Telecom evolution along with typical milestones achieved in the journey of telecom so far
  Typical composition of PSTN network and its topology
  PSTN access network components: Wireline access network and wireless access network
  PSTN terminologies: local loop, signaling , trunk, Central office, LATA, LEC, IXC
  Telephone addressing and routing scheme
  PSTN signaling classification

## Slide 29: Thank You

## Slide 30: Standards, Protocols and Standard Organizations
Notes: Let’s have a look at a small module called ‘Standards, Protocols and Standard Oraganizations’.

## Slide 31: Objectives
At the end of this session, you will be able to:
  Understand the need of standardization and protocols
  Understand the difference between standard, recommendation and protocol
  Understand different national/international standard organization in the field of communication and their achievements
  Understand ITU and internet standards

## Slide 32: Agenda
Standard v/s Recommendation v/s Protocol
Standard Organizations: ISO, ANSI, EIA, IEEE, ITU
Internet standards
Factors affecting communication evolution

## Slide 33: Standards and Protocols
Standard
  Provides a model for development that makes it possible for a product to work regardless of the individual manufacturer
  Standards are developed by co-operation amongst standard creation committees, forums and regulatory agencies
  Standards v/s Recommendations
Protocol
  Set of rules being agreed upon by all parties in communication
  Syntax, Semantics and Timeliness / Logical sequence
Notes: Syntax refers to structure or format of the data, meaning order in which they are presented. Example in a protocol the Address /Control/Data/FCs is the sequence.
Semantics: Semantics refers to meaning of each section of bits.
Timing: Refers to when data to be sent & how fast they can be sent for proper reception.

## Slide 34: Standard Organizations
ISO
  International Standard Organization
  Birth: 1947, Voluntary, Worldwide scope
  Achievement: Invented OSI model
ANSI
  American National Standard Institute
  Private non-profit organization not affiliated to US govt.
  Achievement: ANSI C, ASCII and lot other
EIA
  Electronics Industries Association
  Manufacturers association in US
  Achievement: EIA-232 D and EIA -530 standards

## Slide 35: Standard Organizations
IEEE
  Institute of Electrical and Electronics Engineers
  Research and Development in almost of all area of engineering – lot of research papers
  Largest professional group in development of standards for computing, communication etc.
  It sponsored LAN project
  Achievement: 802.X protocols
Regulatory Authorities
  Review of technical specifications, allocate spectrum, charging control
  FCC – Federal Communication Commission [ US ]
  TRAI – Telephone Regulatory Authority of India

## Slide 36: ITU
The International Telecommunication Union (ITU)
  International organization the oldest UN organization
  was founded in 1865 headquartered in Geneva each UN member country has the right to become a member of the ITU.
Notes: ITU …The International Telecommunication Union (ITU) ..which formerly was knows as CCITT…
It is an International organization with word wide presence. It is the oldest UN organization …founded in 1865 having headquarter in Geneva. Each UN member country has the right to become a member of it.
Under ITU there are various sub divisions called ITU-T …ITU for telephony, ITU-R ..ITU for radio and ITU-D …for development…Beneath every of this there are study and research groups who constantly endeavor for research activities in a particular domain.

## Slide 37: Internet Standards
Internet standard is a Specification thoroughly tested to be followed by those who work with internet
Internet Society is a professional Membership Society that spans more than 100 countries & many organizations
Internet Engineering Task Force(IETF) & Internet Architecture Board (IAB) is part of Internet Society
All Request for comments (RFC) and Internet Standards are developed through these organizations
The MAC address & IP addresses are also issued under internet society

## Slide 38: Factors Affecting Communication Evolution
Technology, Regulation, Markets, Standards
What are FACTS?
Technology
Regulation
Market
Standards
Can it be built?
Will it sell?
Is it allowed?
Will it inter-operate?
Notes:   So let’s end this small modules with the Factors affecting communication evolution.
  There are basically four major factors that can impact communication evolution …Technology, Regulation, Markets and the Standards…
Technology basically talks about …can it be built.. Regulation talks about …it is allowed ? Any operator working any where emitting frequencies in any range of any power …Is this allowed ? Market basically talks about …will it sell ? You have got a technology which technically very powerful but it is not commercially that much successful…A good examples of this is a Satellite phone. Satellite phone is technical success but it is not commercially as attractive to end customer …. And the standard will talk about …will it interoperate ? Because now a days we have got N number of communication technolgoies, technical infrastructures as well as protocols existing…So unless and until they marry with each other …interoperate with each other..communication will very limited and restrictive….It is quite important to note in today’s and future context that ‘Single standalone technology may not survive in a long run …however nice it may be’…. It needs to create a bond with others…
So …Let’s understand some facts !!!
1) Availability of a technology does not mean it will sell. I have already talked about an example called Satellite
phones.
2) It is never very clear beforehand whether a market exists for a product or service…so again a very important thing from a marketting perspective.
3) Regulation authorities and the standards will talk about monopoly…i.e. they would talk about moving away from monopoly in this globalized world…and making that standards essential so that interoperability would be easy …
With this we come towards and end of topic called ‘Standard Protocols and standard organizations’.

## Slide 39: Summary
In this session, we have learned:
  The need of standardization and protocols
  Difference between standard, recommendation and protocol
  Different national/international standard organization in the field of communication such as ISO, ANSI, IEEE, etc.
  ITU and internet standards
  Factors affecting communication evolution

## Slide 40: Thank You

## Slide 41: Basics of Communication and Transmission Media
Notes: Let’s try to understand basic concepts of communication as well as basics of transmission media… So basics of Communication and transmission media..

## Slide 42: Objectives
At the end of this session, you will be able to:
  Understand the signal and its characteristics
  Understand difference between Analogue and Digital signal
  Draw transmission medium classification
  Draw the composition of transmission media used in communication and list its features
  List the advantages of optical fiber communication
  Draw wireless frequency spectrum along with application wise spectrum distribution

## Slide 43: Agenda
Signal characteristics
Signal – Analogue and Digital
Transmission Media classification and features
Fiber optic: Pros and Cons
Frequency spectrum and applications

## Slide 44: Signal
Notes: Everything is communication evolves around a signal…so let’s try to understand more details about the signal…By the way there are two types of signals…one is called analog signal and another is called digital signal…Under analog signal category we have further classification such as periodic signal …the one which is repetative in nature and aperiodic i.e. random signal…
As said early…periodic signal is the one where there is repetation of a signal which is happening after a certain interval of a time…on the contrary in case of aperiodic signal there is no such phenomenon called repeatation…Rather random signals would come under this category…
What is shown in the front is a typical periodic signal called sine wave which all of us are aware of …
Every analog signal has which a periodic signal has got three important characterisgtics – Number 1 …Amplitude, Number 2 …time period of the signal which indirectly denotes the Frequency and Number 3 …Phase…
First and foremost important characteristics of a signal is Amplitude or strength…More is amplitude …more will be peak value and more peak-to-peak value…
Now in this case this particular signal is getting repeated only once in one second …by the way frequency is nothing but number of repeations of signal per second and the unit of freq. is Hz. Because the above signal is getting repeated once we call the frequency of this signal as 1 Hz..But is this signal would have repeated 1000 times …the freq. would have been 1000 Hz or so called 1Khz. On similar fashion, 10 rest to 6 times repeatation in one second gives rise to frequency of 1 Mhz…By the way, if number of repetations are more then the time period of one signal becomes less…so needless to say that frequency is time period of a signal are inversely proportional. More freqency …less time period and vice-varsa…
And the last characteristics is a phase….which talks about where is signal starting…In the present case, signal starts at 0 that is why we say sine of 0 as 0 but in case of COSINE signal it starts at 90…this is called phase of a signal
So the three important attributes of a signal are – amplitude , frequency and phase and one can change one or more of these characteristics…

## Slide 45: Analog Signal: Amplitude and Frequency
Notes: Shown in the figure are two analog periodic signals of different amplitude and frequency…Frequency of signal drawn above is less than the one shown below. Frequency of signal shown below is 6 Hz because it is repeating 6 times a second…

## Slide 46: Digital Signal: Bit Rate and Bit Interval
Notes: This is a typical digitals signal…And unlike analog signal which has infinite amplitude variations , digital signal has only two variations and that is why it is also referred as BINARY signal…
Here you can have amplitude either as 5 volts represented as 1 or 0 volts represented as 0…By the way, here I am taking about TTL level…IN TTL , voltage 5 corresponds to representation 1 and voltage 0 corresponds to representation 0…
A time period for which a particular bit is on or off is called as BIT INTERVAL…It is possible to have bit interval being different but let’s not go that complexity for the time being…In the case shown above, bit interval is same…Now..number of bits which are tranmitted in 1 second is called Bits Per Second or BPS. It is called bit rate…In this case bit rate is 8 bps… Again if you reduce the bit interval , bit rate will be more and vice-varsa…
BPS in digital signal is equivalent to frequency in analog signal..
Now a days we have a CPU of the order of GHz where clock frequency is of the order of 10 rest to 9 per second…
10 rest to 12 is called Tera Hz…

## Slide 47: Transmission Media
Notes: Now lets begin with an important topic called transmission media…
These are the one which will carry the signals…
Classification is as shown in the figure…Guided transmission medium or so called Wired and un-guided or wireless…
Under guided transmission medium we have further classification such as twisted pair , co-axial and fiber where as unguided medium happens to be an air…In twisted pair and coaxial cable data is transferred in terms of electrical signals, in fiber it is transferred in the form if light whereas in air electromagnetic waves are transferred….
By the way, guided medium is also called bounded medium with unguided as unbounded…

## Slide 48: Transmission Medium – Coaxial Cable
Category | Impedance | Use
RG-59 | 75 W | Cable TV
RG-58 | 50 W | Thin Ethernet
RG-11 | 50 W | Thick Ethernet
Notes: Let’s start with co-axial cable…
Explain construction… Shown in the figure is a typical structure of a co-axial cable…
……
It is called co-axial because…
Category and use..
Cable tv v/s computer network cable…

## Slide 49: Transmission Medium – UTP and STP

## Slide 50: Twisted Pair Categories
Category | Bandwidth | Data Rate | Digital/Analog | Use
1 | very low | < 100 kbps | Analog | Telephone
2 | < 2 MHz | 2 Mbps | Analog/digital | T-1 lines
3 | 16 MHz | 10 Mbps | Digital | LANs
4 | 20 MHz | 20 Mbps | Digital | LANs
5 | 100 MHz | 100 Mbps | Digital | LANs
6 | 200 MHz | 200 Mbps | Digital | LANs
7 (draft) | 600 MHz | 600 Mbps | Digital | LANs

## Slide 51: Transmission in Fiber - Optic Cable
Transmits digital signals in the form of pulses of light
Optical carriers are designated according to their transmission capacity
Attenuation is measured in dB/km, which today ranges from 0.2 to 2.0 dB/km
More noise immunity
Critical Angle
Notes: Another very interesting transmission medium called Fiber optic cable…
Transmits digital signals in the form of pulses of light…so need a converter to convert signal in analog form to digital and then to light while sending and reverse process while receiving….
Electical  light …laser .. Light emitting diode
light  Electrical …photo diodes , photo transistors..
Communication medium is glass

## Slide 52: Transmission in Fiber - Optic Cable
Notes: Multi Mode Cable:Multiple beam of light source move thro core in different paths.
Multimode Step Index:Has the density of core remaining constant from center to edges.Sice there is abrupt change in density at the edge due to lower density thus causing a step.This abruptness causes the distortion.
Multimode Graded Index: Here the density of core varies, highest at the center & lowest at the edge. This variable density causes the light to converge at regular intervals. Thus if this convergence is at the receiver the received signal will have better distortion figures compared to Step index.
Single Mode: In this mode the core is manufactured with lower density or index of refraction with lesser diameter of core. This decrease in density results in propagation of beams almost horizontal, thus delay & distortion is minimum. All beams arrive at destination together.Most preferred for long distance communication, but most expensive.

## Slide 53: Fiber : Pros and Cons
Major advantages of Optical Fiber are :
  less Attenuation
  more bandwidth
  data security
  least reaction to chemicals & noise immunity
  storage is Simpler
BUT
  Needs skilled labor to handle joints & each joint adds to losses
  More expensive

## Slide 54: Frequencies for Communication
VLF = Very Low Frequency
LF = Low Frequency (Submarine)
MF = Medium Frequency (AM)
HF = High Frequency (AM)
VHF = Very High Frequency (TV, Mobile)
UHF = Ultra High Frequency (TV, Mobile)
SHF = Super High Frequency (Satellite)
EHF = Extra High Frequency(Satellite)
OPTICAL = Optical Fiber links (IR)
UV = Ultraviolet Light
1 Mm
300 Hz
10 km
30 kHz
100 m
3 MHz
1 m
300 MHz
10 mm
30 GHz
100 m
3 THz
1 m
300 THz
visible light
VLF`
LF
MF
HF
VHF
UHF
SHF
EHF
infrared
UV
optical transmission
coax cable
twisted pair

## Slide 55: Summary
In this session, we have learned:
  Signal – Analog and Digital, their characteristics
  Difference between Analogue and Digital signal
  Classification of transmission media
  Composition, characteristic features and speed/bandwidth of bounded media such as coaxial and twisted pair copper and fiber
  Advantage of fiber optic communication medium over others
  Wireless frequency spectrum with application wise spectrum distribution

## Slide 56: Thank You

## Slide 57: Transmission Parameters
Notes: Let’s being a discussion on another small module called ‘Transmission Parameters’…

## Slide 58: Objectives
At the end of this session, you will be able to:
  Understand different transmission parameters and their impact on communication
  Understand the definition of bandwidth and comparison of bandwidth of different communication media
  Understand transmission parameters called attenuation
  Understand various forms of noise in communication, their impact on transmission, measurement of SNR and remedy if any

## Slide 59: Agenda
Transmission parameters and their impact on communication
Bandwidth
Attenuation
Noise
SNR

## Slide 60: Transmission Parameters
Bandwidth
Attenuation
Noise
Crosstalk
External interference
Notes: There are different transmission line parameters that affect the transmission of a signal…
Out of which no.1 bandwidth of transmission medium can affect ..
No.2. attenuation of a signal when a signal traverses through transmission medium
No.3 noise …4 cross talk and the last one is external interference…
So let’s have a look at one by one…

## Slide 61: Bandwidth
Range of frequencies that can be carried across a given transmission channel
Notes: Bandwidth… bandwidth of communicaiton channel is nothing but range of frequencies that can be carried across a given transmission channel
So with this , every tranmission medium has some limit on highest frequency components that can be passed through without any distortion…
None of the communication medium has got infinite bandwidth..Shown towards the left side of the figure is a picture depicting increase in the bandwidth as you go from twisted pair to fiber…Technically bandwidth is nothing but highest frequency component – lowest frequency component. Assuming that lowest frequency component to be zero, bandwidth of communication channel is equal to highest frequency component…
Shown on the right side a typical human voice bandwidth i.e. what human can speak….having maximum frequency component of 4Khz so we say bandwidth of human voice as 4 KHz in the idel condition. However, real usable bandwidth of human voice is from 300Hz to 3300 Hz i.e. 3 KHz…Even air as communication medium has got such a bandwidth that it can transmit extreme low to extreme high frequencies. Radio , TV and satellite communication uses air as a communication channel….Optical fiber can transmit signals in Terahertz range…
So in nut shell bandwidth of such communication media is so high that to utilize it to an optimism extent , we always send multiple signals through the same medium by using a technique called multiplexing which we will see soon…

## Slide 62: Bandwidth and its Impact on Transmission
Transmission Medium Signal Corruption
Notes: This is another example of bandwidth…Highest freq. component is 5000 and lowest one is 1000 , so bandwidth is 5000-1000 which is equal to 4000…
By the way, shown below is a digital signal square wave being passed thorough transmission medium which gets distorted when passed through because digital signal can be though of as sum of infinite collection of sine and cosine waves of different frequency , amplitude and phase. This is a basis for fourier series which was explained by a scientist called fourier. And none of the communication medium has infinite bandwidth so that they can pass on digital signal as it is…And that is presizely what has happened above….few of high frequency components which could not get through the communication medium ,so they got lost and that is why the shape of the signal at the output side…Solution to this problem is given by a phenomenon called Modulation which we will see soon..

## Slide 63: Attenuation
Attenuation
  Opposite of amplification
  Reduction of signal strength
  Signal becomes unintelligible
  Measured in decibels
analog signal amplification
digital signal regeneration
Notes: Attenuation ..Attenuation manifests itself as a reduction of the signal's amplitude in the receiver. Attenuation is Opposite of amplification and it is something to do with reduction of signal strength…When you pass the signal through any transmission medium, because of the characteristics of the medium, signal strength gets reduced. This reduction factor depends on the type of communication medium. It is least in fiber optic and most in Air. Analogy…hitting a ball on the ground…ground offers resistance and slows down the speed of ball…If ground would have been resistance less then ball would have traversed infinitely…which is practically not possible…
Because of this phenomenon signal strength is reduced to such an extent that signal becomes unintelligible …so there is need of amplification…Shown on left side a typical amplification process and right below is the same one in digital context… Note that in CN context, this amplifier is called as repeater….By the way , amount of attenuation is always measures in decibels.
Here we should understand one thing that attenuation is in nobody’s hand… none of the transmission media are ideal …moreover transmission media are passive in nature..…so attenuation is a part of life…and repeater or amplifiers are required if we want to send signal towards much longer distance…

## Slide 64: Noise - Bit Error
Notes: Another factor affecting transmission is noise…so let’s try to understand this attribute
Also it is worth to mention that communucation media being passive and non-intellegent, can not differentiate between noise and a signal…so it is not the duty of communication medium to resist the noise… It is duty of end equipments and protocols embeded therein to make sure that WHAT IS SENT IS WHAT IS RECEIVED. To tackle this, we must have error detection and error correction techniques built in at both end equipments or protocols…
Noise factor varies across the communication media ….In air it is maximum whereas in fiber optic it is minimum…but we cannot say, that the error can not happen…

## Slide 65: Noise
External Noise
  Man-made noise
    Generated by equipment such as motors.
  Atmospheric noise (also called static)
    Dominates at lower frequencies .
  Space noise (Mostly solar noise)
    Dominates at higher frequencies and can be a serious problem in satellite communications.
Internal Noise
  Thermal noise (also called white noise)
    Is produced by random motion of electrons in a conductor due to heat.
    Noise Power in watts is directly proportional to Bandwidth in Hz, and the temperature in degrees Kelvin.
Notes: Typical classification of noise called ‘External noise’ or Internal noise is shown in the figure…
Under external noise category we have ….so and so …. Which you can not eliminate …Radio TV really needs to take care of this…

## Slide 66: Signal-to-Noise Ratio (SNR)
Signal-to-Noise Ratio (SNR)
  Ratio of signal power to noise power
  Is expressed in decibels
  SNR (dB) = 10 log10 (PS/PN)
  PS is the signal power in watts PN is the noise power in watts
Notes: How to evaluate a communication system from a noise perspective ? So solution towards this is SNR…Signal to Noise ratio…. Communication system is said to be better if SNR is more…
Explain SNR eqn…
tell that Pn not in controll, so what you can control is Ps ..signal power. If we want more power, we need to have powerful amplifiers…

## Slide 67: Example
Imagine a signal travels through an amplifier and its power is increased ten times. This means that P2 = 10 * P1. In this case, the amplification (gain of power) can be calculated as
10 log10 (P2/P1) = 10 log10 (10P1/P1)
= 10 log10 (10) = 10 (1) = 10 dB

## Slide 68: Summary
In this session, we have learned:
  Different transmission parameters and their impact on communication
  Definition of bandwidth and comparison of bandwidth of different communication media
  Transmission parameters such as attenuation, noise and their impact on transmission and remedy
  Definition and formula of SNR

## Slide 69: Thank You

## Slide 70: Digital Communication
Notes: Let’s begin a discussion on Digital Communication

## Slide 71: Objectives
At the end of this session, you will be able to:
  Understand digital signal representation and its characteristic features
  Understand the need of digital transmission and edge over analogue counterpart
  Understand the process of analogue to digital conversion called PCM – Pulse Code Modulation
  Understand quantization step in PCM, quantization error and its impact on quality of digital quality

## Slide 72: Agenda
Digital Signal characteristics
Advantage of digital transmission
Analogue to Digital conversion process

## Slide 73: Digital Signal: Bit Rate and Bit Interval
Notes: Digital signal can be thought of as series of 1’s and 0’s.
We have already seen concepts like bit interval, bit rate and so on…

## Slide 74: Why Digital Transmission?
Technology
  Drop in COST, shrink in SIZE as well as POWER due to LSI,VLSI technology
Capacity utilization
  Digital techniques can more easily and cheaply utilize available transmission links of high bandwidth through multiplexing
Better noise immunity
Security and privacy
Compression and decompression
Source independent !!!
Error detection & correction methods can be used
In general, more efficient & reliable means of communication
Notes: Technology: Sees a drop in cost due to LSI and VLSI
Capacity utilization : Digital techniques can more easily and cheaply utilize, through multiplexing, available transmission links of high bandwidth. Security and privacy: Encryption techniques are more readily applied to digital data

## Slide 75: PCM Process
Notes: A/D conversion technique called Pulse Code Modulation PCM involves following processes:
  Sampling/Pulse Amplitude Modulation (PAM)
  Quantization: which when combined with sampling, allows for representing Analog signal in Discrete form.
  Compression forms an important part in Quantization.
  Corresponding TO NA/Europe we have μ-law or A-law compression techniques.
  Encoding process: To translate the discrete set of sample values to a more appropriate form of signal.
  Transmitting: Sending the bits in suitable form by using line coding techniques
PCM generator produces a series of numbers, or digits.Each one of these digits(in binary code) always represents the approximate amplitude of the signal sample at that instant.

## Slide 76: Quantized PAM Signal
Quantizing by using sign and magnitude

## Slide 77: Summary
In this session, we have learned:
  Digital signal representation and its characteristic features
  The need of digital transmission and edge over analogue counterpart
  Process of analogue to digital conversion called PCM – Pulse Code Modulation
  Quantization error and its impact on digital quality

## Slide 78: Thank You

## Slide 79: Modulation Demodulation
Notes: Let’s start with PSTN Introduction..By the way PSTN stands for Public switch telephone network

## Slide 80: Objectives
At the end of this session, you will be able to:
  Understand the need and process of modulation/demodulation
  Understand difference between analogue and digital modulation techniques
  Understand analogue modulation techniques called AM, FM along with applications
  Understand digital modulation techniques called ASK, FSK and PSK and their variants along with applications
  Understand the functionality of MODEM

## Slide 81: Agenda
Need of modulation
Concept of Modulation
Modulation Techniques in Analog and Digital domain
AM, FM
ASK, FSK and PSK
Modem

## Slide 82: Carrier and Modulation
Carrier
  Carriers are exclusively analog in nature
  Generally of high frequency
Modulation
  Process of changing one of the characteristics of carrier wave viz. amplitude or frequency or phase in proportion to amplitude of the input wave is called ‘Modulation’ process.
Notes: Modulation Means of controlling the characteristics of a signal in a desired way.
Carrier signal A high frequency signal used for digital-to-analog or analog-to-analog modulation. One of the characteristics of the carrier signal (amplitude, frequency or phase) is changed according to the modulating data.
In analog signal, the sending device produces a high frequency signl that acts as a basis for the information signal. This base signal is called the carrier signalor carrier frequency. The receiving device is tuned to the frequency of the carrier signal that it expects from the sender. Digital information is then modulated on the carrier signal by modifying one or more of its characteristics (amplitude, frequency, phase). This kind of modification is called modulation (or shift keying) and the information signal is called a modulating signal.
Modulation:Modification of one or more characteristics of a carrier wave by an information bearing signal.
Demodulation The process of separating the carrier signal from the information bearing signal.
Analog-to-Analog Conversion
Often an analog signal is sent over long distances using analog media. For example, voice or music from a radio station, which is naturally an analog signal is transmitted through the air. However, the frequency of the voice or music is not appropriate for this kind of transmission : the signal should be carried by a higher frequency signal. This is called analog-to-analog conversion. Analog to analog modulation can be accomplished in three ways Amplitude Modulation (AM), Frequency Modulation (FM) and phase modulation (PM).
Amplitude Modulation (AM) In AM transmission, the carrier signal is modulated so that its amplitude varies with the changing amplitudes of the modulating signal. The frequency and phase of the carrier remain the same; only the amplitude changes to follow variations in the information. The modulating signal becomes an envelope to the carrier. The bandwidth of an AM signal is equal to twice the bandwidth of the modulating signal and covers a range centered around the carrier frequency. The bandwidth of an audio signal (speech and music) is usually 5KHZ. Therefore, an AM radio stations needs a minimum bandwidth of 10 KHz. AM stations are allowed carrier frequencies anywhere between 530 and 1700 KHz (1.7 MHz). However, each stations carrier frequency must be separated from those on either side of it atleast by 10KHz to avoid interference. If one station uses a carrier frequency of 1100 KHz, the next stations carrier frequency cannot be lower than 1110 KHz.
FM Modulation In FM transmission, the frequency of the carrier signal is modulated to follow the changing voltage level(amplitude) of the modulating signal. The peak amplitude and phase of the carrier signal remain constant, but as the amplitude of the information signal changes, the frequency of the carrier changes correspondingly. The bandwidth of an audio signal (speech and music) broadcast in stereo is almost 15KHz. Each FM radio station, therefore needs a minimum bandwidth of 150 KHZ. The FCC allows 200 KHz(0.2 MHz) for each station to provide some room for guard bands.FM stations are allowed carrier frequencies anywhere between 88 and 108 Mhz. Stations must be separated by atleast 200 KHz to keep their bandwidths from overlapping.

## Slide 83: Analog Modulation: AM
AM Radio
  One carrier one radio channel
  Each channel requires 10 KHz
  Frequency range 530 KHz to 1700 KHz

## Slide 84: Analog Modulation: FM
FM Radio
  One carrier one radio channel
  Each channel required 200 KHz
  Frequency range 88 MHz to 108 MHz
Notes: Better noise immunity than AM

## Slide 85: Digital Modulation

## Slide 86: Modulation: B-ASK and B-FSK

## Slide 87: Modulation: B-PSK

## Slide 88: Modulation: QPSK

## Slide 89: MODEM – MOdulator DEModulator

## Slide 90: Summary
In this session, we have learned:
  The need and process of modulation/demodulation
  Difference between analogue and digital modulation techniques
  Analogue modulation techniques such as AM, FM along with applications
  Digital modulation techniques called ASK, FSK and PSK and their variants along with applications
  Functionality of MODEM

## Slide 91: Thank You

## Slide 92: Multiplexing Techniques and PSTN Hierarchy

## Slide 93: Objectives
At the end of this session, you will be able to:
  Understand the need of multiplexing/demultiplexing
  Classify multiplexing techniques
  Understand TDM, FDM and WDM multiplexing techniques w.r.t. concept, scheme, pros and cons
  Draw and understand Plesiochronous Digital Hierarchy (PDH) used in American and European standard
  Understand the difference between digital trunk lines T1, T2, T3 and T4 / E1, E2, E3 and E4

## Slide 94: Agenda
Need of multiplexing
Multiplexing techniques classification
Time Division Multiplexing [TDM]
Frequency Division Multiplexing [FDM]
Wavelength Division Multiplexing [WDM]
Plesiochronous Digital Hierarchy (PDH)-European and American standard

## Slide 95: Multiplexing Techniques
Transmitting several entities on the same physical medium (such as a wire pair or air)
  Time Division Multiplexing (TDM)
  Frequency Division Multiplexing (FDM)
  Wavelength Division Multiplexing (WDM)
Notes: Multiplexing is used to reduce transmission costs - several channels along the same route share the same transmission medium, such as optical fibre
By the way, why is multiplexing required ?
Explain concept of sharing and how to use shared medium ?

## Slide 96
Frequency Division Multiplexing
S2
S3
S4
S5
S6
S1
f
t
c
Notes: Separation of the whole spectrum into smaller frequency bands
A channel gets a certain band of the spectrum for the whole time

## Slide 97
Analog Mux hierarchy

## Slide 98: FDM : Multiplexing and De-multiplexing
Advantages
  no dynamic coordination necessary
  works also for analog signals
Applications
  Radio , TV
Disadvantages
  waste of bandwidth if the traffic is distributed unevenly
  guard spaces required
Notes: Analogy is : Express high way with lanes where is multiple cars are going simultaneously…In a sense, here bandwidth of road is divided..

## Slide 99
Time Division Multiplexing

## Slide 100
Time Division Multiplexing

## Slide 101
24-Channel PCM/TDM Process
Notes: Advantages
  only one carrier in the medium at any time
  throughput high even for many users
Disadvantages
  precise synchronization necessary
  Wastage of bandwidth of if nothing present at that timeslot
Applications
  Telephony

## Slide 102: Wavelength Division Multiplexing [WDM]
Prisms in WDM multiplexing and demultiplexing
What do you divide here ?

## Slide 103
Wavelength Division Multiplexing

## Slide 104: Plesiochronous Digital Hierarchy (PDH)
Time division multiplexing in PSTN
Why two different systems across the world?
Notes: The NA & Europeans decided on 2 different compression techniques base on μ-Law & A-law respectively.
This led to 2 different incompatible PCM systems throughout the world.

## Slide 105
Digital Trunks - T1 T2 and T3

## Slide 106: Difference between a T1 and DS1
T1 defines a physical attribute of a transmission system operating at 1,544 Mb/s
  Cabling
  Regenerator Spacing
  Connectors
DS1 defines a 1.544Mb/s digital signal format
  Pulse shapes
  Frame Format
A T1 carrier typically carries a DS1 Signal
A DS1 may also be carried with a higher rate multiplex system such as DS3 or SONET
Notes: Now one question that often comes up at this point is T1, and DS1. It is known that they both operate at 1.5 Mb/s, so they say, "Well, what's the difference between the two? Why do I need two words to mean the same thing?” It turns out that they are oftentimes confused, or oftentimes used interchangeably; but there is a difference between them, that if you use them properly, you can avoid some confusion.
T1 refers to the physical transport facility. So, for example, T1 is the connectors, the cabling, the repeater spacing—all the things you need to electrically send the signal at 1.5 Mb/s over twisted wire pair. So we're sending this 1.544 million b/s signal over twisted wire pair using T1 electronics.
Digital Signal Level 1(DS1), is a particular signal format operating at that same 1.5 Mb/s rate. So DS1defines things like the pulse shapes and their spacing, and the framing format and channelization. So in essence, T1 Carrier defines the electrical system to carry the signal; DS1 defines the actual signall. Where you start seeing differences is, for example, a T1 line operating at 1.5 Mb/s, carry a signal format other than a DS1. Similarly, a DS1 signal can be carried on physical facilities other than aT1; for example, over a radio link.
Also, as I go up to the transmission hierarchy— a DS3 carries 28DS1 signals, but it's not carrying any T1s because a T1 is a physical facility . So for a DS3 (which is carried on a T3, by the way) I could have coming in 28 T1s, each of those 28 T1s, is carrying a DS1 signal. I take those DS1 signals off of the T1s, multiplex them together to form a DS3 signal that we'll then carry on a T3.
So the T is the physical facility and its implementation; the DS is the actual signal format that you're carrying. The DS will go on other kinds of physical facilities; the T is a fixed type of physical facility.

## Slide 107: Digital Trunks - E1 E2 E3 and E4
Notes: End of the session…

## Slide 108: Summary
In this session, we have learned:
  Need of multiplexing/demultiplexing
  Classification of multiplexing techniques
  TDM, FDM and WDM multiplexing techniques w.r.t. concept, scheme, pros and cons
  Plesiochronous Digital Hierarchy (PDH) used in American and European standard
  Difference between digital trunk lines T1, T2, T3 and T4 / E1, E2, E3 and E4

## Slide 109: Thank You

## Slide 110: PSTN Switching
Notes: Let’s begin with another module called ‘PSTN Switching’…

## Slide 111: Objectives
At the end of this session, you will be able to:
  Understand the need of switching and definition of switching
  Understand the notion of circuit switching and the role of switch in PSTN network
  Draw classification of switching and historical evolution in telecom switching
  Understand block schematic of a typical digital exchange
  Understand notion of time and space switching
  Understand steps followed in end-to-end telephone call
  Understand types of PSTN nodes and their interconnectivity

## Slide 112: Agenda
Switching and Switch
Classification of telecom switches
Digital exchange
Telephony: A typical end-to-end call flow
PSTN nodes and interconnectivity

## Slide 113: ITU-T Definition of Switching
The ITU-T defines switching as:
“The establishing, on demand, of an individual connection from a desired inlet to a desired outlet within a set of inlets and outlets for as long as is required for the transfer of information".
Notes: Here is a classical ITU-T definition of switching…

## Slide 114: Circuit Switching
Notes: PSTN uses circuit switching where as computer network uses packet switching. Let’s understand , What is meant by circuit switching.
Circuit switching creates a direct physical connection between two devices. By moving the lever of the switches , any telephone on the left side can be connected to any telephone on the right side. To be very specific and perfect , circuit switching reserves resources between end to end entities. Resource in PSTN context is a time slot.
Circuit switch is a device with n inputs and m outputs that creates a temporary connection between input link and output link. The number of inputs does not have to match with number of outputs.
Circuit switching today either use either of two technologies : Space division switches OR time division switches.

## Slide 115: Switching
Switch
  Device that sets up a communication path on demand and tears it down when it is no longer needed
Switching
  Routing information between different parties
Digital
Time division
Space division
Strowger
Crossbar
Analog
Switches
Manual
T & S
Notes: Switch …Device that sets up a communication path on demand and tears it down when it is no longer needed
The switching systems can be classified into three categories;
Manual - where all operation was manual
Analog - where operation was automatic but information transfer was analog
Digital switches where operation was automatic and information transfer was digital.

## Slide 116: Manual Switching Systems
Manual Switching :
Conversation with
operator
Notes: Exchanges have undergone revolutionary change starting from Manual till today’s automatic electronic exchange/switch.
Beginning of this revolution started with Manual exchange wherein all operations carried out manually by human operators sitting in front of switch board especially dominated by women as seen in the figure.
But as the subscriber densities increased the need for automatic exchange was felt and strowger was the one who invented first ever automatic exchange which replaced human operators.

## Slide 117: Strowger Switching System
Notes: The construction of strowger exchange involved two-motion selector as shown in the figure.
Selectors used are constructed using electromechanical rotary switches.
Exchange transmitted sound in the form of analog signals.
Since Strowger eliminated the operator, the calling customer must provide the pulses to drive the selector. The number of pulses in a train is equal to the digit value it represents except in the case of zero, which is represented by 10 pulses.
Operation :
When the digit 5 is dialed, five pulses are generated by the subscriber’s handset and transmitted to the strowger switch.
The switch then steps to level 5. and then subscriber dialed 6 wherein switch steps horizontally for the second digit dialled which in this case is 6 and connection is established.

## Slide 118: Crossbar Switching
Crossbar Switches by G. A. Betulander - designed using Common Control Concept
Notes: Disadvantages
  Expensive relays
  Noise due to chattering of delays
  Limited capacity due to grid

## Slide 119: Electronic Exchange
Notes: Electronic Exchange or Digital switches are the one where operation are automatic and information transfer was digital.
Conversion of analog to digital and vice-varsa happens here. Information traversal between such exchanges in digital in nature.
Typical advantages of these type of changes are :1) Faster call setup and tear down, 2) Optimum utilization of resources , 3) better quality and error control

## Slide 120: The Subscriber Stage

## Slide 121: Block Diagram of SLIC for a Digital Exchange
(BORSCHT Function)
B BATTERY FEED
O OVER VOLTAGE PROTECTION
R RINGING
S SUPERVISORY SIGNALLING
C CODING(CODEC)
H HYBRID
T TESTING
Test
Access
Test
Equipment
Ringing
Ring
Trip
Overload
Protection
Battery
Feed
Off-Hook
Supervision
HYBRID
CODER
DECODER
TX
RX
Two wire
Sub’s Line
Digital Switch
SLIC Functions

## Slide 122
Time and Space Switch
Notes: Delete this slide…

## Slide 123: Time Slot Interchange Time Switching Technique
Time slot
counter
Speech
memory
Control
memory
Read address
Write address
23
24
2
1
1 2 24
1 2 24
1
2
24

## Slide 124: Phase 1: The A-subscriber lifts the handset

## Slide 125: Phase 2: The exchange receives the B-subscriber number

## Slide 126: Phase 3: The exchange sets up the outgoing calls

## Slide 127: Phase 4: The subscribers conclude their conversation

## Slide 128: PSTN Nodes
PSTN nodes can be subdivided into three main categories:
  Local exchanges
  Transit exchanges
  International exchanges
Notes: PSTN nodes
PSTN nodes can be subdivided into three main categories: local exchanges, transit exchanges and international exchanges. Local exchanges are used for the connection of subscribers. Transit exchanges switch traffic within and between different geographical areas. International exchanges, and other gateway-type exchanges, switch traffic to telecommunications networks that belong to other operators.

## Slide 129: Exchange Hierarchy
Another look : Voice Network Heirarchy
Higher traffic ,
higher switching speed ,
higher bandwidth
Class 5
Class 1
E1/ T1 Links
E4/ T3 Links
Notes: This is another classification of exchange hierarchy. Theme is same names are changed.
Basic Principle remains same.
Higher is the level , higher is the load so is switching speed so is bandwidth requirement.

## Slide 130: PSTN Network Architecture
Access
40,000
MegaStream
sites
Tier 3
2000 - 6500
nodes
Tier 2
500 nodes
Tier 1
60 nodes
Tier 2
Large towns
Tier 3
Small towns
& suburbs
Tier 1
cities
Access

## Slide 131: Summary
In this session, we have learned:
  Need of switching and definition of switching
  Notion of circuit switching and the role of switch in PSTN network
  Classification of switching
  Historical evolution in telecom switching
  Block schematic of a typical electronic exchange
  Time and space switching concept
  End-to-end telephone call: Step by step
  Types of PSTN nodes and their interconnectivity to form PSTN network architecture

## Slide 132: Thank You

## Slide 133: Signaling in Communication

## Slide 134: Objectives
At the end of this session, you will be able to:
  Understand the need of signaling and its categorization
  Understand the types of signaling used in PSTN: CAS, CCS
  Understand the need of CCS over CAS
  Understand common signaling standard called ‘SS7 signaling system’ from a perspective of features and advantages
  Understand SS7 network architectural components such as SSP, SCP and STP and their roles
  Understand PSTN call flow with SS7 network

## Slide 135: Agenda
Signaling classification
Channel Associated Signaling [CAS]
Common Channel Signaling [CCS]
SS7 signaling network features
SS7 signaling network architecture
PSTN call flow using SS7 network

## Slide 136: Signaling
Request service from the central office switch
Provide central office switch with the information necessary to route a telephone call
Alert destination address of incoming call
Provide status information and call supervision for billing.
Manage network lines/trunks

## Slide 137: Signaling Categories
CO
CO
1. Off Hook
Supervisory
5. Ring
5. Alerting
4. Seizure
4. Wink
4. Control
3. 555-2345
3. Address
2. Dial Tone
2. Information
Notes: Supervisory Signals are from subscriber to initiate or terminate the call or to invoke the facility(offhook onhook)
Information Signal is from exchange to subscriber indicating the progress of the call (tones)
Address Signal from subscriber to exchange or between the exchanges gives the called party number of the facility (destination)
Control Signal between switches to initiate or terminate the call.
Alerting Signal from switch to subscriber indicating the arrival of the call.

## Slide 138: Dial Methodologies
Pulse Dialing
Tone Dialing
Notes: Dial tone , ring tone , off hook , on hook are couple of other examples of subscriber local loop signalling.

## Slide 139: Signaling Context

## Slide 140: Inter Exchange Signaling

## Slide 141: Channel Associated Signaling
Line signaling in time slot 16
Channel associated Signaling - Line signaling
Frame 16
Frame 1
Multiframe
16
16
16
16
Signaling for time
slots 15 and 31
Signaling for time
slots 2 and 18
Signaling for time
Slots 1 and 17
Multiframe alignment
16
Notes: Signaling in circuit-switched networks - Old signaling systems may also use traffic channels for signaling Signalling is slow
Information capacity is limited and used inefficiently
Limited or no capacity for non call-related information
Applies to telephony only - cannot cover new services
Signalling capacity reserved for the slot

## Slide 142: Common Channel Signaling [CCS]
Notes: The most modern form of interexchange signalling on circuit-switched connections is common channel signalling (CCS). SS7, which belongs to this category, is predominant in modern digital networks. CCS requires a separate signalling network; that is, the signals have a bearer service of their own. Because the signalling network executes this bearer service, it can be accessed by users other than the PSTN. Other typical users are ISDN and the PLMN.

## Slide 143: CCS/SS7 FEATURES/Advantages
Features:
  SS7 network is a packet switched network
  Voice channel is dedicated for voice and information signals such as dial tones and announcement
  Signaling channels are on separate network
  Signaling channels carry control, address and supervisory signals
  Signaling network is common to all voice channels
Advantages:
  Greater volume of signaling information with added flexibility
  Reduction in call set up times
  More efficient use of trunks
  Reduction in fraud rate due to separation of signaling and voice path
  Facilitation of additional (transaction based) services

## Slide 144: SS7 Network Elements
IP
Service Switching Point
Notes: The Service Swiching point or the SSP are telecom switches equipped with SS7-capabile software. They are used to originate, terminate or switch calls

## Slide 145: SS7 Network Elements
IP
Signaling Transfer Point
Notes: The Signal Transfer Points or the STP receive and route the incoming signaling messages towards the proper destination. They also perform specialized and complex routing functions

## Slide 146: SS7 Network Elements
IP
Signaling Control Point
Notes: The Signaling Control Point or the SCP is a specialized node in the network that hosts the software and the data for services like
1-800 numbers i.e. toll free numbers
Local number portability , calling cards , prepaid etc. Note that a database is associated with SCP

## Slide 147: SS7 Network Elements
IP
Intelligent Peripheral
Signaling Link
Notes: The Intelligent Peripheral or the IP is the node that provides the IVR (interactive voice resource) functionalities. It plays announcements and prompts and collects user information.
All the nodes in an SS7 network are connected via signaling data links with varied specification.

## Slide 148: Basic ISUP Signaling
Notes: Sequence of call set up.
1.IAM = Initial Address message .required destination number is sent to destination SSP via its own STP by reserving a Trunk (Ckt no5 in this case).
2.Upon confirming the required number is available the destination side SSP2 confirms to calling SSP1 by a ACM=Address complete message through its own associated STP,by reserving the Trunk ckt 5..
Called party fed Ring by SSP2 while SSP1 after receiving ACM feeds Ring back tone (RBT) to Calling party.
3.When called subscriber Answers by lifting his hand set SSP2 sends ANM=Answer Message to SSP1 & removes ring to called subscriber.SSP2 upon receiving ANM removes the RBT to caller & now both parties will be connected by SSP1/SSP2 on Ckt 5.
4.When either party disconnects(in figure party1 disconnects) a REL = Release message is sent to destination SSP(SSP2) asking for release of call by disconnecting CKt 5.
5.SSP2 after disconnection sends back a RLC =Release complete message to SSP 1 Confirming release of Circuit.
Ckt 5 is now available for other calls

## Slide 149: Summary
In this session, we have learned:
  Need of signaling and its categorization
  Types of signaling used in PSTN: CAS, CCS
  CCS v/s CAS
  SS7 CCS: Features and advantages
  SS7 network architectural components such as SSP, SCP and STP and their role in networking
  PSTN telephone call flow using SS7 network

## Slide 150: Thank You

## Slide 151: ISDN, GSM, GPRS and CN
Notes: Let’s have a tour of some advanced technologies such as ISDN …GSM …GPRS and TCP/IP

## Slide 152: Objectives
At the end of this session, you will be able to:
  Understand ISDN network from a perspective of network components and different ISDN flavor of services
  Understand the concept of cell and impact of cell size in GSM
  Understand frequency reuse concept in GSM
  Understand GSM network evolution, network architectural composition and GSM identifiers
  Understand the steps followed in Mobile registration, mobile originated call [MOC] and mobile terminated call [MTC]
  Understand the concept of roaming in GSM
  Understand GPRS network enhancement on the top of GSM
  Understand the role of SGSN and GGSN in GPRS network
  Understand the features of GPRS network
  OSI and TCP/IP protocols, devices and addresses
  Understand the logical and physical representation of internet today
  Understand the dataflow transfer in computer network with applications of mail transfer

## Slide 153: Agenda
ISDN network: features, network, flavors
GSM Network: Cell size and its impact
GSM Network architecture
GSM identifiers
GSM call scenarios: Mobile registration, MOC and MTC
GPRS network architecture
Computer Network: LAN, MAN, WAN
OSI and TCP/IP protocol
Networking devices and addresses
Internet: Physical layout
Client and Server: Mail protocol example

## Slide 154: ISDN
Fax
(group 4)
Network
Terminal
Basic Rate
access
Passive
bus
Terminal
adapter
Primary Rate
access
2B+D
30B+D
PSTN
PSPDN
N - ISDN
NT2
PBX
TA
NT1
WHY ISDN?
What is ISDN?
I : Integrated S : Services
D: Digital N : Network
ISDN is a High speed, Fully digital, Telephone service; Easily controllable and configurable End to End Digital service in PSTN
All at the COST of a bit more MONEY

## Slide 155: ISDN Flavors (Interfaces)
Basic Access consists of two full-duplex 64Kbps B Channels and a full-duplex 16 Kbps D channel. (2B + 1 D)
The total bit rate is 144 kbps.
Framing synchronization, and other overhead bits bring the total bit rate on a basic access link to 192 Kbps.
Primary Access is intended for users with greater capacity
In US and Japan, (23 B + 1 D) 1.5 Mbps is the standard rate i.e. T1
In Europe, (30B +1 D + 1 Sync ) = 2.048 Mbps is the standard rate i.e. E1
Notes: ======
The basic service is intended to meet the needs of most individual users, including residential subscribers and very small offices.
It allows simultaneous use of voice and several data applications, such as internet access, a link to central alarm service, facsimile, teletex and so on.
These services could be accessed through a single multifunction terminal or several separate terminals.
In either case, a single physical interface is provided. Most existing two-wire local loops can support this interface.
Primary Access is intended for users with greater capacity requirements, such as offices with a digital PBX or a LAN.
The U.S., Canada, and Japan makes use of a transmission structure based on 1.544 Kbps; this corresponds to the T-1 transmission facility of AT&T.
In Europe, 2.048 Mbps is the standard rate, both of these data rates are provided as a primary interface service.
Typically, the channel structure for the 1.544 Mbps rate will be 23 B channels plus one 64 Kbps D Channel and the 2.048 Mbps rate, 30 B Channels plus one 64 Kbps D Channel.
It is possible for a consumer with lesser requirements to employ fewer B Channels, in which case the channel structure is nB+D, where n ranges from 1 to 23 or from 1 to 30 for the two primary services.
A customer with high data rate demands may be provided with more than one primary physical interface.
In this case, a single D channel on one of the interfaces may suffice for all signaling needs, and the other interfaces may consist solely of B Channels ( 24B or 31 B).
The primary interface may also be used to support H Channels.
Some of these structures include a 64 Kbps D Channel for control signaling. When no D channels are present, it is assumed that a D channel on another primary interface at the same subscriber location will provide any required signaling.

## Slide 156: ISDN Interfaces
Fax
(group 4)
Network
Terminal
Basic Rate
access
Passive
bus
Terminal
adapter
Primary Rate
access
2B+D
30B+D
PSTN
PSPDN
N - ISDN
NT2
PBX
TA
NT1
Notes: Terminal Equipment refers to subscriber equipment that makes use of the ISDN.
Terminal Equipment Type 1 (TE1) refers to devices that support the standard ISDN interface.
Terminal Equipment Type 2 (TE2) encompasses existing non-ISDN equipment. Such equipment requires a terminal adapter (TA) to plug into an ISDN interface.
NT2 so called Network terminator 2 is a customer premises switching equipment installed by service provider at customer premises.
NT1 (subscriber line terminator) …

## Slide 157: Wireless World - GSM and GPRS
Notes: Let’s move onto GSM and GPRS which almost everybody of us are familiar with ….

## Slide 158: Cellular Implementations Wireless Mobile History
First-generation (1G):
  Analog cellular systems ( 450-900 MHz)
  FDMA for spectrum sharing
  NMT (Europe), AMPS (US)
Second-generation (2G):
  Digital cellular systems ( 900MHz, 1800 MHz)
  TDMA/FDMA/CDMA for spectrum sharing
  Circuit switching in wireless
  GSM (Europe), IS-136 (US), PDC (Japan)
2.5G: Packet switching extensions
  Voice + Data
  Digital: GSM to GPRS
3G:
  High speed and real time data services
  IMT-2000
Notes:     1G systems (analogue) : TACS (UK), AMPS (USA)
    2G systems (digital) : GSM (Europe), TDMA (USA)
    2½G systems : GPRS (Europe)
    3G systems : UMTS (Europe), CDMA 2000 (USA), TD-SCDMA (China)
      aiming for a global standard to allow worldwide roaming but unlikely to happen

## Slide 159: Conventional Mobile Phone Service
Notes: Cellular Concept: Motivation
Early mobile radio systems used to have large coverage with single, high-powered transmitter.
Because of the finite spectrum allocation to an operator and no frequency re-use due to interference limits the customer base.
Need was : High capacity i.e. more number of users with limited spectrum as well as wide coverage.
And the Solution was Cellular mobile …i.e. divide large area into smaller cells

## Slide 160: Cellular Telephone Service: Mobile- to-Mobile
PTC _ PITA Telecoms Conference & Exhibition
Base Station
Cell
Cell
Cell
MTSO
Cell

## Slide 161: Cellular Radio – Infinity illusion
Ideally, 3 different frequency sets are sufficient
A combination of SDM, FDM and TDM
Two separate frequency bands used for Tx and Rx
Sender and receiver sequences shifted by 45MHz and 3 time slots
Predefined time slot for signaling channel
Each communication 200 Khz uplink and 200Khz downlink

## Slide 162: GSM Uplink Downlink
0
124
0
124
890MHz
915MHz
935MHz
960MHz
UPLINK
DOWNLINK
  GSM900 : 880 - 915 MHz paired with 925 - 960 MHz
  GSM1800 : 1710 - 1785 MHz paired with 1805 - 1880 MHz
  GSM1900 : 1850 - 1910 MHz paired with 1930 - 1990 MHz

## Slide 163: 2G Mobile: Frequency Split
PTC _ PITA Telecoms Conference & Exhibition
Base Station
Fre. 7,8,9
Fre. 4,5,6
Cell
MTSO
Fre. 1,2,3
Fre. 13,14,15
Fre. 10,11,12
Fre. 4,5,6

## Slide 164: Cell Size

## Slide 165: GSM: System Architecture
Notes: Gateway Mobile Services Switching Center ( GMSC)
  Point of call entry into the PLMN (for calls terminating in this network from PSTN or other mobile network)
Mobile Switching Center / Visitor Location Register (MSC/VLR)
  Usually integrated in one box
  High Capacity Switch
  Works like a normal exchange
  Responsible for
    Setting up & controlling voices calls & SMS
    Handover & Location Update
    Charging and accounting
Base Station Controller (BSC)
  Handles all BTS under observation
  Manages the radio network and handover from one cell to another
Base Transceiver Station (BTS)
  Responsible for sending and receiving radio signals to / from mobiles
  Quality Measurements and Power Control
Mobile Station (MS)
  Two parts
    Mobile Equipment = Phone instrument
    SIM card = Subscriber Identity Module, a smart card
Home Location Register (HLR)
  Database that stores and manages subscription related information
  Semi-Permanent Data
    Mobile number, SIM number, services
  Dynamic Data
    VLR identity, active services like forwarding
Authentication Center (AuC)
  Database of authentication keys , ciphering keys and algorithms for both authentication and ciphering
  one record per SIM card
Equipment Identity Register (EIR)
  Maintains Mobile Equipment’s serial number
  In terms of
    Black List
    Grey List
    White List
ExTRA Notes
=======
GMSC
Gateway Mobile Services Switching Center
Like a normal exchange
Point of call entry into the PLMN (for calls to mobile)
Interrogates HLR for identifying current location of the mobile
Routes call to the MSC where the mobile is present
Has charging and accounting functions built
MSC/VLR
Mobile Switching Center / Visitor Location Register
Usually integrated in one box
Like a normal exchange
Responsible for
  Setting up & controlling calls including SS & SMS
  Handover & Location Update
  Controlling the BSC
  Equipment Identity Control
  Charging and accounting
BSC
Base Station Controller
Handles all BTS
Manages the radio network
Manages connectivity to Mobile stations including handovers
Administers the BTS & the radio characteristics
Works like a remote unit (slave-switch) of the MSC/VLR
BTS
BTS stands for Base Transceiver Station
Radio equipment responsible for sending and receiving radio signals to / from mobiles
Quality Measurements
Power Control
Broadcasting system information & paging
Receiving channel requests from mobile
Implements radio hopping
MS
Mobile Station
Two parts
  Mobile Equipment = Phone instrument
  SIM card = Subscriber Identity Module, a smart card
Radio equipment
Signaling and speech coding
signal strength measurements
Power Control
HLR
Home Location Register’
Database that stores and manages subscription related information
  Semi-Permanent Data
    Mobile number, SIM number, services
  Dynamic Data
    VLR identity, active services like forwarding
Handles interrogation for locating a mobile
Charging function
Authentication of access
AuC
Authentication Center
Database of authentication keys and authentication algorithms
Contains one record per SIM card
Generates a random number, a ciphering key (for encryption) and a signed response
Authentication is performed in MSC
Ciphering is performed by the BTS
Implementations vary
EIR
Equipment Identity Register
Maintains Mobile Equipment’s serial number
Maintains three lists
  Black List
  Grey List
  White List
Consults the lists and returns information of which list the mobile is on
Used for controlling calls from stolen mobiles and faulty mobiles

## Slide 166: GSM Identifiers
MSISDN
  Mobile Station ISDN number
  Number that can be dialed from a mobile/telephone
  Country Code (CC) + Network Destination Code (NDC) + Subscriber Number (SN)
IMSI
  International Mobile Subscriber Identity
  Unique identity of a SIM card / subscription
  Mobile Country Code (MCC) + Mobile Network Code (MNC) + Mobile Subscriber Identification Number (MSIN)
  The key field for billing
TMSI
  Temporary Mobile Subscriber Identity
  Security mechanism
  Avoids usage of IMSI as an identity over the air
  Allocated by MSC
IMEI
  International Mobile Equipment Identity
  Unique identity of hand-set
LAI
  Location Area Identity
  Key element for location update
Notes: IMEI : Type Approval Code (TAC) + Final Assembly Code (FAC) + Serial Number (SNR) + Software Version Number (SVN)
LAI : Mobile Country Code (MCC) + Mobile Network Code (MNC) + Location Area Code (LAC)
With this we come to an end of GSM network. Now let’s have a look as GPRS network.

## Slide 167: Mobile Registration
Wherever you go our Network catches you
Wherever mobile moves, the entry will be registered into the MSC/VLR in context and Pointer to VLR is stored in HLR
In the nutshell, HLR is a single point of contact for every mobile

## Slide 168: Mobile Terminated Call [MTC]
PSTN
calling
station
GMSC
HLR
VLR
BSS
BSS
BSS
MSC
MS
1
2
3
4
5
6
7
8
9
10
11
12
13
16
10
10
11
11
11
14
15
17
1: calling a GSM subscriber
2: forwarding call to GMSC
3: signal call setup to HLR
4, 5: request MSRN from VLR
6: forward responsible MSC to GMSC
7: forward call to
current MSC
8, 9: get current status of MS
10, 11: paging of MS
12, 13: MS answers
14, 15: security checks
16, 17: set up connection

## Slide 169: Mobile Originated Call [MOC]
PSTN
GMSC
VLR
BSS
MSC
MS
1
2
6
5
3
4
9
10
7
8
1, 2: connection request
3, 4: security check
5-8: check resources (free circuit)
9-10: set up call
Paging is NOT necessary in this call

## Slide 170: Roaming
What happens in Roaming?
  In a roaming scenario, mobile user moves from home network and go in some other operator’s network and wanted to use services [may be incoming or outgoing]
  In such scenarios, based on IMSI , operator would get to know as to which country and which operator a subscriber belongs to
  Roaming network checks whether subscriber is allowed to roam by asking HLR of the home network and seek the information
  If answer received is Yes, then subscriber is allowed else subscriber is denied
What is the difference between National and International roaming?
  National roaming  Operator other than home within a country
  International roaming  Operator other than home outside a country

## Slide 171: GPRS Architecture
SS7
BTS
BSC
MSC
VLR
HLR
AuC
GMSC
BSS
PSTN
NSS
A
E
C
D
PSTN
Abis
B
H
MS
BSS Base Station System
BTS Base Transceiver Station
BSC Base Station Controller
NSS Network Sub-System
MSC Mobile-service Switching Controller
VLR Visitor Location Register
HLR Home Location Register
AuC Authentication Server
GMSC Gateway MSC
SGSN Serving GPRS Support Node
GGSN Gateway GPRS Support Node
GPRS General Packet Radio Service
IP
2G+ MS (voice & data)
PSDN
Gi
SGSN
Gr
Gb
Gs
GGSN
Gc
Gn
2G MS (voice only)
GSM towards GPRS transition
Notes: GPRS stands for General Packet radio service. It is overlaid network on already existing GSM network with modification of component for GPRS compliance. With GPRS network , now one can have data services like www , ftp , mail , mms along with traditional GSM services like voice and SMS with GPRS enabled mobile.
GGSN
Serves as the interface to external IP networks which could be TCP/IP or X.25 network which see the GGSN as an IP router serving all IP addresses of the MSs
GGSN stores current SGSN address and profile of the user in its location register
It tunnels protocol data packets to and from the SGSN currently serving the MS
It also performs authentication and charging
GGSN can also include firewall and packet-filtering mechanisms
SGSN
Analog of the MSC in GSM
Routes incoming and outgoing packets addressed to and from any GPRS subscriber located within the geographical area served by the SGSN
Location Register of the SGSN stores information (e.g. current cell and VLR) and user profiles (e.g. IMSI, addresses) of all GPRS users registered with this SGSN

## Slide 172: GPRS Architecture
SS7
BTS
BSC
MSC
VLR
HLR
AuC
GMSC
BSS
PSTN
NSS
A
E
C
D
PSTN
Abis
B
H
MS
BSS Base Station System
BTS Base Transceiver Station
BSC Base Station Controller
NSS Network Sub-System
MSC Mobile-service Switching Controller
VLR Visitor Location Register
HLR Home Location Register
AuC Authentication Server
GMSC Gateway MSC
SGSN Serving GPRS Support Node
GGSN Gateway GPRS Support Node
GPRS General Packet Radio Service
IP
2G+ MS (voice & data)
PSDN
Gi
SGSN
Gr
Gb
Gs
GGSN
Gc
Gn
2G MS (voice only)
Notes: GPRS stands for General Packet radio service. It is overlaid network on already existing GSM network with modification of component for GPRS compliance. With GPRS network , now one can have data services like www , ftp , mail , mms along with traditional GSM services like voice and SMS with GPRS enabled mobile.
GGSN
Serves as the interface to external IP networks which could be TCP/IP or X.25 network which see the GGSN as an IP router serving all IP addresses of the MSs
GGSN stores current SGSN address and profile of the user in its location register
It tunnels protocol data packets to and from the SGSN currently serving the MS
It also performs authentication and charging
GGSN can also include firewall and packet-filtering mechanisms
SGSN
Analog of the MSC in GSM
Routes incoming and outgoing packets addressed to and from any GPRS subscriber located within the geographical area served by the SGSN
Location Register of the SGSN stores information (e.g. current cell and VLR) and user profiles (e.g. IMSI, addresses) of all GPRS users registered with this SGSN

## Slide 173: GPRS Features
Voice + data together
Higher data rate support
Provides connectivity to external packet data networks
Enables many users to share radio resources by dynamic, on-demand, multi-slot allocation
Modification to the GSM air-interface
Addition of new GPRS Support Nodes, SGSN, GGSN
Enables volume-based charging as well as duration based charging
Notes: Always on
Circuit switching for voice and packet switching for data

## Slide 174: Power of Technology
Low Power
Short Range
High Power
Long Range
Low Data Rate
High Data Rate
GSM/2G
GPRS/2½G
UMTS/3G
Text
Graphics
Internet
Audio
Video
Multi-channel
Video
2G, 2.5G and 3G comparison
Notes: Edge : Just after GPRS 1) A method of increasing the data rates on the radio link for GSM 3-4 times increase in data speeds over GPRS claimed
2) Different protocols and behaviour in the Base Station System same packet handling protocols in the core network
3) Introduces a new modulation technique and new channel coding scheme
UMTS (3G)
1) To cope with increasing volumes of traffic
and new capacity-demanding apps such as video streaming & music download
2) Developed as a global standard to assure international roaming
though now unlikely to be universal e.g. USA, China may use different standards
3) A development from GSM and CDMA – also known as W-CDMA
4) Auction of licenses for spectrum
  extremely expensive to set up the new infrastructure needed
5) New handsets required : dual purpose handsets – have to be back-operable with GSM
With this we come towards an end of GPRS network. Now let’s have a look at computer network.

## Slide 175: Computer Network
Computer Network
  Interconnected collection of Autonomous computers
  Collection: group of computers
  Interconnected: via media - Wired or wireless
  Autonomous: independent
What is main purpose behind it?
  Sharing of information
  Sharing of resources
Notes: Autonomous … totally independent …democracy ….every body has equal access

## Slide 176
OSI Layer Functions

## Slide 177
Network
Data Link
Physical
Transport
Session
Presentation
Application
Network
Data Link
Physical
Transport
Session
Presentation
Application
Data
Encoded Data
Data
Data
H
Data
H
H
Data
H
H
H
T
10101000110101
Data
H
H
H
T
Data
H
H
Data
H
Data
Data
Decoded Data
OSI Layer
END To END
Data transfer
process
Notes: Data Encapsulation
        Application Layer - User interacts with the application he is using.
        Presentation Layer - User data is encoded.
        Session Layer - It transfers the data to transport layer while doing the token control
        Transport Layer - It adds its own header and thus data segment is formed
        Network Layer - It also adds its own header thus forming the packet
        Data link Layer - It adds a header and tailer thus forming frame
        Physical Layer - It transmits data in form of stream of bits
Data Decapsulation
        Physical Layer – It passes the incoming stream of bits to the data link layer
        Data link Layer - It removes the data link header and tailer and passes the packet to the network layer
        Network layer - It removes network layer header and passes the data to the transport layer
        Transport layer - It removes transport header recognizes the data belongs to which application and passes the data to the session layer
        Session layer - It passes the data in encoded form to the presentation layer
        Presentation layer- It does the decoding and passes the data to the application layer
        Application layer - The user at the application layer receives the data

## Slide 178: LAN: Topology
Network Topology
Refers to the arrangement or physical
layout of computers, cables and other
components on the network
Standard Topologies
LAN - Bus , Star , Ring , Mesh , Hierarchy
WAN – Mesh and hierarchy
Notes: Based on scale and authority , there is a classification of networks called LAN, MAN and WAN
LAN is collection of computers/devices in a small area especially a campus of a company/institute. It has got a single authority for control.
Arrangement of computers/devices is called Network topology.
LAN uses “share a medium” mechanism so demands for protocols as to how to share. Unlike static multiplexing schemes like TDM,FDM etc. LAN uses dynamic multiplexing schemes. Famous amongst them is CSMA/CD ….Polite protocols , democracy – every body has equal right to access , sense for silence before you speak…If you find somebody speaking , abstain from specking .,…characteristics of Politeness. Nevertheless this is not the only protocol.
LAN : Topology used in LAN can be ….BUS ,Ring , Star , Hierarchy ….but preferred ones are star and Hierarchy

## Slide 179: Architecture of the Internet: Physical View
LAN WAN Divide
LAN WAN Divide
Notes: WAN is interconnection of LAN with the help of device on the edge of LAN called router. Routers are connected to each other using point to point links and they are arranged in combination of graph and tree to have good amount of redundancy as well as quick transfer by using shortest path.
Interconnection of routers at various hierarchical levels forms the backbone of Internet.

## Slide 180: Internet Today

## Slide 181: Internet USA Structure

## Slide 182: TCP/IP and OSI Model
Router – Routing and addressing
End to end reliable data transfer
Framing , error control , flow control and hop-to-hop delivery
End Applications
Raw bits transmission
Notes: When we want two heterogeneous systems to talk with each other there has to be protocol between them.
What is protocol ? Protocols are rules and procedures agreed upon by all parties for communication.
The TCP/IP protocol reference model was used in the ARPANET and is still in use in its successor, the worldwide Internet.
It came to be known as the TCP/IP model after its two primary protocols: TCP and IP. It was first defined in 1974.
It the only language talked on Internet. By the way TCP/IP is not a single protocol but a suite of protocols. As you could see in above diagram at every layer there are certain protocols.
There are other standards/protocols existing.
ISO’s i.e. Indian standard organizations OSI protocol suite
IBM Systems Network Architecture (SNA)
Novell NetWare
Apple's AppleTalk
It is interesting to note that : TCP IP is a real implementation whereas ISO’s OSI is a model and on time line TCP/IP came first.
Application , Presentation and Session layer of OSI are kind of clubbed into one in TCP/IP and is known as application layer.
Functionalities of each layer are as shown in figure.
Presentation : Encryption and compression
Session : Maintain a session between two end entities

## Slide 183: Connecting Devices
Router – Routing and addressing
Bridge/ Layer 2 switch
Notes: Router works at layer 3. Its main function is addressing and routing.
Bridge in a multiprotocol router within a LAN. It can understand multiple data link layer protocols.
Repeater and hub are physical layer devices. They do not have much intelegence as routers or switches do have.

## Slide 184: Address and Context

## Slide 185: TCP/IP: How Data is Transferred?
`
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
Router

## Slide 186: Client-Server Paradigm
Client:
Initiates contact with server (“speaks first”)
typically requests service from server
Server:
Provides requested service to client.
Always on
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
Request
Reply
Typical client-server protocols in Internet: Telnet, FTP, HTTP, POP, SMPT etc.
Router
Notes: Typical network app has two pieces: client and server

## Slide 187: How Mail is Transferred?
Notes: Some examples of command-driven user agents are mail, pine, and elm
Some examples of GUI-based user agents are Eudora, Outlook, and Netscape.
Give example of Tech Mahindra server system

## Slide 188: Summary
In this session, we have learned:
  ISDN network components and different ISDN services such as PRI, BRI
  Concept of cell and frequency reuse in GSM
  GSM network evolution, network architectural composition and GSM identifiers
  Process of Mobile registration, mobile originated call [MOC] and mobile terminated call [MTC]
  Roaming in GSM
  GPRS network enhancement on the top of GSM
  Role of SGSN and GGSN in GPRS network
  GPRS network features
  OSI and TCP/IP protocols, network devices and addresses
  Logical and physical representation of internet today
  Concept of client and server with example of mail transfer

## Slide 189: Thank you

## Slide 190: Broadband – An Overview
Notes: Let’s have a tour of various technologies in a broadband such as DSL, Frame Realy, SONET and ATM…
The main objective here is to get familiarize with different terms used in this area.

## Slide 191: Objectives
At the end of this session, you will be able to:
  Understand the notion of broadband
  Understand DSL overview and typical ADSL network composition
  Understand ‘what is SONET/SDH system’, a typical SONET system network composition, SONET device layer relationship and SDH network segments
  Compare SONET and SDH
  Understand design goal of ATM along
  Understand ATM layers and ATM network architecture
  Understand ATM cell format and ATM adaptation layers

## Slide 192: Agenda
Broadband introduction
DSL and ADSL
What is SONET/SDH?
SONET system
SONET v/s SDH
ATM: Design goals
ATM network architecture
ATM cell format

## Slide 193: Broadband in Brief
Type of telecommunications
Uses a wide band of frequencies (channels) to transmit & receive information
Uses high order multiplexing (many channels into one channel)
Transmits data concurrently with voice on many different frequencies within the band
Analogy: More lanes on the highway allow more cars to pass so more passengers to travel at the same time
Notes: What is broad band ?… Let us have a brief understanding of broadband…
Broadband is a type of telecommunication
Broadband uses wide band of frequencies (channels) to transmit/receive information.
Broadband uses very high order multiplexing…..Multiplexing is a technique which we use in telecommunication to club many channels into one..
Broadband transmits data concurrently with voice on many different frequencies within the band.
Analogy of a broadband can be given like this… There are many lanes on the highway to allow more cars to pass so more passengers to travel at the same time. SO we have very high data rate …we go in for a broad band…
Broadband uses different technologies like optical fiber, DSL, terrestrial wireless or even satellite communication…
Broadband mostly uses circuit switched network …this is a speciality of broadband…
Many new technologies are evolving and are at the primitive stage today which will be used in near future…
Typical applications involve video-on-demand, high speed data which includes graphics, movies, animations… download, video conferencing, on-line learning across the globe etcetra…

## Slide 194: Broadband in Brief (Contd…)
Uses different technologies like optical fiber, DSL, terrestrial wireless or satellite
Mostly uses a Circuit Switched Network
Many new technologies are evolving and are at the primitive stage today
Typical applications involve video-on-demand, high speed data (graphics, movies, animations) download, video conferencing, on-line learning across the globe
Notes: What is broad band ?… Let us have a brief understanding of broadband…
Broadband is a type of telecommunication
Broadband uses wide band of frequencies (channels) to transmit/receive information.
Broadband uses very high order multiplexing…..Multiplexing is a technique which we use in telecommunication to club many channels into one..
Broadband transmits data concurrently with voice on many different frequencies within the band.
Analogy of a broadband can be given like this… There are many lanes on the highway to allow more cars to pass so more passengers to travel at the same time. SO we have very high data rate …we go in for a broad band…
Broadband uses different technologies like optical fiber, DSL, terrestrial wireless or even satellite communication…
Broadband mostly uses circuit switched network …this is a speciality of broadband…
Many new technologies are evolving and are at the primitive stage today which will be used in near future…
Typical applications involve video-on-demand, high speed data which includes graphics, movies, animations… download, video conferencing, on-line learning across the globe etcetra…

## Slide 195: DSL Overview
Frequency
D – Internet
Notes: Now, let’s try to understand how DSL is used in broadband…
DSL is one of the technology which is used in broadband…
What is DSL ?…DSL means Digital Subscriber Line… It was invented by Bellcore, USA…. It was aimed at bandwidth of 2 Mbps over current copper network.
DSL requires two modems, one at the Telco’s end and the other at the subscribers end.
It also requires D SLAM. A D SLAM is usually found in the Central Office (Exchange). DSLAM combines multiple xDSL access lines into one high speed line..
DSL services are dedicated, point-to-point, public network access over twisted-pair copper wire on the local loop (“last mile”) between a network service provider (NSP) central office and the customer site (maximum 5.5 km).
In DSL Voice & data travel simultaneously over the same line.
The entire bandwidth available on copper is ~ 1 MHz. The xDSL technologies take advantage of this added bandwidth (above 4 KHz) and uses these upper frequencies for data services. Previously this was not possible because of the interference. Advances in Digital Signal Processing (DSP) have eliminated the near-end cross talk.
The term xDSL covers: ADSL, SDSL, HDSL, RADSL and VDSL.
Voice from PSTN or data from Internet goes through xDSL line cards and reach every house by POTS network. At the subscriber’s end splitter is used to split the voice and data. Voice enters telephone and data enters the computer.
Let us talk about ADSL …ADSL stands for Asymmetric Digital Subscriber Line
ADSL can literally transform the existing public information network from one limited to voice, text and low-resolution graphics to a powerful, ubiquitous system capable of bringing multimedia, including full motion video to every house.
ADSL technology is asymmetric. It allows more bandwidth downstream and less bandwidth upstream. Downstream means from Service Provider’s central office to the customer site.
This asymmetry, combined with always-on access (no call set up), makes ADSL ideal for net-surfing, video-on-demand and remote LAN access.
ADSL transmits more than 6 Mbps to a subscriber. This expands existing capacity by a factor of 50 or more without new cabling.

## Slide 196: Digital Subscriber Line – ADSL Configuration
ADSL | : | Asymmetric Digital Subscriber Line
DSLAM | : | Digital Subscriber Line Access Multiplexer
NID | : | Network Interface Device
Notes: ADSL provides higher bit rate from network towards subscriber(down Stream) than the Upstream data (user to Network) Hence it is called Assymetric.It uses the same Local loop of Copper that is used for conventional POT.
However the factors such as distance between switch & the user & size of cable all matter for Quality of service.
The achievable data down stream is 8Mbps while on upstream it is 1Mbps.

## Slide 197: SONET / SDH
Notes: Let’s move on to another technology …SONET/SDH

## Slide 198: What is SONET / SDH?
SONET stands for Synchronous Optical Network. It is the ANSI standard used in North American network
SDH stands for Synchronous Digital Hierarchy. It is the ITU-T standard. Has become Global standard & SONET is subset of SDH.
SONET / SDH is a synchronous network. A single clock is used to handle the timing of transmission and equipment across the entire network. It is highly predictable system. It also has a very powerful frame design.
SONET / SDH is high speed, low cost system
Notes: What is SONET or SDH ? …Why it is an important technology ?…
SONET stands for Synchronous Optical Network….It is the ANSI standard
SDH stands for Synchronous Digital Hierarchy….It is the ITU-T standard.
SONET or SDH is a synchronous network. A single clock is used to handle the timing of transmission and equipment across the entire network.
It is highly predictable system….It also has a very powerful frame design….SONET/SDH is high speed, low cost system.
SONET/SDH contains recommendations for the standardization of fiber optic transmission system equipment sold by different manufacturers….
SONET/SDH is flexible to carry signals from incompatible tributary systems like DS-0, DS-1 etc.
SONET is a multiplexed transport mechanism….SONET can be a carrier for Broadband services , particularly ATM and B-ISDN.

## Slide 199: What is SONET / SDH? (Contd…)
SONET / SDH contains recommendations for the standardization of fiber optic transmission system equipment sold by different manufacturers.
SONET / SDH is flexible to carry signals from incompatible tributary systems like DS-0, DS-1 etc.
SONET / SDH is a multiplexed transport mechanism.
SONET / SDH can be a carrier for BB services, particularly ATM and B-ISDN
Notes: What is SONET or SDH ? …Why it is an important technology ?…
SONET stands for Synchronous Optical Network….It is the ANSI standard
SDH stands for Synchronous Digital Hierarchy….It is the ITU-T standard.
SONET or SDH is a synchronous network. A single clock is used to handle the timing of transmission and equipment across the entire network.
It is highly predictable system….It also has a very powerful frame design….SONET/SDH is high speed, low cost system.
SONET/SDH contains recommendations for the standardization of fiber optic transmission system equipment sold by different manufacturers….
SONET/SDH is flexible to carry signals from incompatible tributary systems like DS-0, DS-1 etc.
SONET is a multiplexed transport mechanism….SONET can be a carrier for Broadband services , particularly ATM and B-ISDN.

## Slide 200: A SONET System
Notes: SONET relies on three basic devices: The diagram shows a complete SONET system…
At the lower leftnmost side we have STS MUX and At the rightmost side we have STS DEMUX
STS MUX : multiplexes the signals from multiple sources into an STS signal or STS demultiplexer demultipluxex STS signal into different destination signals.
Regenerator … It is a repeater that takes optical signal and regenerate it.
ADD/DROP MUX …ADM…. They can add signals coming from different sources into a given path or remove a desired signal from a path and redirect it without Demuxing the entire signal.

## Slide 201: SONET Device-Layer Relationship
SONET Layers
Notes: SONET defines four layers…
The photonic layer is the lowest …and performs …physical layer activities.
The section, line and path layers correspond to the OSI model’s data link layer.
The diagram shows the relationship between the devices used in SONET transmission and the four layers of the standard.
STS Multiplexer is a a four layer device.
ADD/DROP Multiplexer is a three layer device.
A Regenerator is a two layer device.

## Slide 202: SDH Network Segments
SDH -EMBEDDED OVERHEAD CAPABILITIES
PATH OVERHEAD CAPABILITIES
MULTIPLEXER SECTION OVERHEAD CAPABILITIES
REGENERATOR SECTION OVERHEAD CAPABILITIES
SDH
TERMINAL
MULTIPLEXER
SDH
TERMINAL
MULTIPLEXER
TRIBUTARY
SIGNALS
TRIBUTARY
SIGNALS
VC
ASSEMBLY
VC
DISASSEMBLY
PATH
SDH
CROSS-CONNECT
SYSTEM
SDH
REGENERATOR
MULTIPLEXER
SECTION
REGENERATOR
SECTION
REGENERATOR
SECTION
REGENERATOR
SECTION
MULTIPLEXER
SECTION
Notes: VC-Virtual Container ( pay Load)

## Slide 203: SONET / SDH
Difference between SONET/SDH:
  There are some differences in the basic frame format between the two Standards
  SDH & SONET are identical beyond the STS-3 signal level
  The base signal for SONET is STS-1 and the base signal for SDH is STM-1
  STS-3 is equivalent to STM-1 and the lower tributaries can be mapped inter-changeably between the two format from that point onwards
  The definition of Path in both the standards are same but the following difference exist:
    SONET uses Line/Section for defining path
    SDH uses Repeater/Multiplexer sections for defining path
  The transmission rates vary and are same from STS3/STM-1 onwards

## Slide 204: SONET / SDH Rates
STS | OC | Rate(Mbps) | STM
STS-1 | OC-1 | 51.840 | ――
STS-3 | OC-3 | 155.520 | STM-1
STS-9 | OC-9 | 466.560 | STM-3
STS-12 | OC-12 | 622.080 | STM-4
STS-18 | OC-18 | 933.120 | STM-6
STS-24 | OC-24 | 1244.160 | STM-8
STS-36 | OC-36 | 1866.230 | STM-12
STS-48 | OC-48 | 2488.320 | STM-16
STS-96 | OC-96 | 4976.640 | STM-32
STS-192 | OC-192 | 9953.280 | STM-64
STS – Synchronous Transport Signal
OC – Optical Carrier
STM – Synchronous Transport Module

## Slide 205: ATM
Notes: Let’s end out discussion with another interesting technology called ‘ATM’…
By the way, ATM stands for Asynchronus Tranfer Mode…
It is a Cell Relay protocol designed by the ATM forum and adopted by ITU-T…

## Slide 206: Why ATM?
Design Goals:
Optimization of the use of high-data-rate transmission media especially Optical Fiber
A system that can have interface with the existing systems for wide area connectivity
Inexpensive
The new system should work with existing telecom hierarchies (local loops, long distance carriers etc.)
The system should be connection-oriented to ensure accurate and predictable delivery
To move as many functions to hardware as possible
Notes: What are the design goals of ATM ?….
There are many design goals of ATM …The first and the most important amongst them is ..
Optimization of the use of high-data-rate transmission media especially Optical Fiber. In addition it offers a large bandwidth …
The second design goal is a system that can have interface with the existing systems for wide area connectivity…As we know..ATM is basically used for WAN applications…and so the interfaces are very important…
Third …it is an inexpensive technology…
Fourth ….The new system should work with existing telecom hierarchies ….For example ….local loops, long distance carriers etc.
Fifth….The system should be connection-oriented to ensure accurate and predictable delivery
And the last one I.e. sixth ….To move as many functions to hardware as possible
So there were goals in mind when ATM was designed…

## Slide 207: Multiplexing - Different Perspectives
Multiplexing Using Cells
Multiplexing Using Different Packet Sizes
ATM Multiplexing
Notes: Cell Network: It uses the cell as a basic unit of data exchange. A cell is defined as a small fixed sized block of information. All data are loaded into identical cells that can be transmitted with complete predictability and uniformity. All cells are then multiplexed with other cells and routed through the cell network. This avoids the problem of multiplexing different sized packets.
Let us try to understand what are Cell Networks and how ATM multiplexing is done ? …
ATM is made of cells the way we have packets in IP network…Only difference is cell is of fixed size where as IP packet is of variable size….
…It uses the cell as a basic unit of data exchange.
A cell is defined as a small fixed sized block of information.
All data are loaded into identical cells that can be transmitted with complete predictability and uniformity.
All cells are then multiplexed with other cells and routed through the cell network.
This avoids the problem of multiplexing different sized packets and so the predictability is very high…
ATM is asynchronous TDM I.e. Time Division Multiplexing… It uses fix sized slots. ATM mux. fills the slot with a cell from any input channel that has a cell; the slot remains empty if none of the channels has a cell to send.
For example. You see in the diagram …there is a multiplexer and there are 3 channels …Channel 1 , Channel 2 and Channel 3
Channel 1 has 3 slots …A1 , A2 and A3…which are filled with cells…
Channel 2 has 2 slots …B1 and B2
And finally Channel 3 has again 3 slots …C1, C2 and C3…
Now all the channels are fed to a multiplexer…Look at the output of a multiplexer…First it goes to A1, then C1,
then A2, followed by B1 , followed by C2 and so on….
Here between A1 and C1 the slot of was empty …but the output of the multiplexer is not empty …because it has bypassed that slot… This is how ATM multiplexer works…

## Slide 208: ATM Multiplexing
Asynchronous Transfer Mode - ATM, attempts to combine the best of both worlds -- the guaranteed delivery of circuit-switched networks and the robustness and efficiency of packet-switching networks.

## Slide 209: ATM Layers and Cells
Notes: Now let us see what are ATM layers and how they are used …
In ATM there are 3 standard layers defined…
From top to bottom …they are Application layer or to be very specific AAL …Application Adaptation Layer…..then we have ATM layer and then Physical layer...
The diagram shows it very clearly…
By the way, each cell of ATM is of 53 bytes out of which 5 bytes is header and remaining 48 bytes are left for payload or data…

## Slide 210: ATM Architecture
Notes: What is ATM architecture ?
ATM is a cell switched network.
The user access devices are called as end points are connected through a UNI, user-to-network interface to the switches inside the network. You can see them in the diagram at extreme left and extreme right…
The switches are connected through network-to-network interfaces (NNI) this is shown in the middle of the diagram..
ATM switches are shown in the yellow blocks…All yellow boxes I.e. ATM switches are connected using NNI …

## Slide 211: TP, VPs and VCs
Notes: Let us try to understand what are TPs , VPs and VCs in the context of ATM ?
TPs are transmission paths …Connection between two end points is accomplished through these TPs
Transmission path …TP …is a physical connection which can be wire , cable or satellite connection…
Between end point and switch or between two switches…
What are VPS ? VPs is nothing but virtual paths … Transmission path is divided into Virtual Paths as shown in the figure …
Virtual path provides a connection or set of connection between two switches…
Think of virtual path as a highway …that connects two cities.. A set of all highways is a transmission path…
Now …let us study what are VCs…..VCs are nothing but virtual circuits…All cells belonging the same message follow the same virtual circuit…
and remain in their original order until they reach the destination … Think of virtual circuit as the lanes of express high way…
Figure shows a clear cut relation TP, VPs and VCs…
By the way, between end point and Switch there is a VC and between two switches there is VP…

## Slide 212: ATM Cell Format
Notes: GFC-Generic Flow control-provides flow control at UNI level.
VPI: Virtual Path Identifier
VCI-Virtual Circuit Identifier
PT-Pay Load Type.
CLP: Cell loss priority which is provided for congestion control.A cell with CLP 1 is retained as long as there are cells with a CLP = 0.

## Slide 213: ATM Adaptation Layers
AAL1: Constant bit rate data – For Video conferencing /Interactive audio and
  A/V distribution and retrieval
AAL2: Variable bit rate data – For compressed Audio/Video/Fax
AAL3/4: Connection oriented/Connection less data services – Has comprehensive sequencing & error control
AAL5: Mix of all the above – Does not have the comprehensive sequencincing & error control

## Slide 214: Summary
In this session, we have learned:
  What is broadband
  DSL overview and typical ADSL network composition
  What is SONET/SDH system
  SONET system network composition, SONET device layer relationship
  SDH network segments
  Comparison between SONET and SDH
  Design goal of ATM along
  ATM layers and ATM network architecture
  ATM cell format and ATM adaptation layers

## Slide 215: Thank You

## Slide 216: Bluetooth, Wi-Fi and Wi-Max
Notes: Let’s move on to wireless access technology area and try to understand technologies such as BlueTooth, Wi-fi and Wi-max at an abstract level…

## Slide 217: Objectives
At the end of this session, you will be able to:
  Classify IEEE wireless standards along with their range of operations
  Understand bluetooth network at a very conceptual level
  Understand Wi-Fi andWi-Max network from a perspective of network composition, working and applications
  Compare Wi-Fi and Wi-Max network

## Slide 218: Agenda
IEEE wireless standards
Bluetooth
Wi-Fi
Wi-Max
Comparison of Wi-Fi and Wi-Max

## Slide 219: Wireless Puzzle
Notes: The wireless Puzzle !!!
There are lot of jargens and standards in the wirelss access areaad.
Some of them have been depicted in this area like….VSAT, Bluetooth , 8o2.15 , 802.11 , gprs , wi-max , umts etc…

## Slide 220: IEEE Wireless Standards
WAN (Mobile)
802.20
MAN (Metro)
802.16
LAN (Local)
802.11
PAN (personal)
802.15
Wi-Max: 802.16
Wi-Fi: 802.11a/b/g
Bluetooth: 802.15
Notes: Wireless standards ….
IEEE has specified different standards in …different access areas …This is a pictorial representation of different wireless technology standards…
The picture shows that …how range and …coverage various across various IEEE wireless standards…
The standard which works at smallest range and coverage is PAN …I.e. personal aread network…it is also called as WPAN…Bluetoothe operates in this area..Technically this standard is known as eight o two dot fifteen…
Moving up the chain…wireless lan network which is also called as Wi-Fi. Where IEEE 802.11 standard flavors are operating …
Is is also called WLAN ..Wireless LAN…
Then we have Wirelss Man network …or so called WMAN…It is also called as Wi-Max standard…and IEEE standard is 802.16 …
And above it the WWAN I.e. Wireless WAN where IEEE standard eight o two dot twenty is present

## Slide 221: Bluetooth Technology
Bluetooth wireless technology is a short-range communications technology intended to replace the cables connecting portable and/or fixed devices while maintaining high levels of security.
Works in unlicensed spectrum
Standard
  IEEE 802.15
Notes: Blue tooth technology ….
Bluetooth is a wireless technology
It’s a short-range communications technology…intended to replace the cables connecting portable and/or fixed devices while maintaining high levels of security.
..Used by mobiles devices such as phones , computers and PDAs
Blue tooth predominantly operates in the unlicensed spectrum of 2.45 Ghz Freq band
The diagrams shows how blue tooth enables devices such as C< laptop, PDA and handicam interact with each other
IEE Standard for blue tooth is IEEE 802.15

## Slide 222: Wi-Fi
Wi-Fi (Wireless Fidelity) is a generic term that refers to the IEEE 802.11 communications standard for Wireless Local Area Networks (WLANs)
Wi-Fi Network connect computers to each other, to the internet & to the wired network
Uses licensed & un-licensed spectrum based on range
Standards
  IEEE 802.11a
  IEEE 802.11b
  IEEE 802.11g
Notes: Now we move onto another wireless standard called Wi-FI…
Wi-Fi is an acronym of Wireless Fidelity
Wi-Fi is a generic term that refers to the IEEE 802.11 communications standard for Wireless Local Area Networks (WLANs).
Wi-Fi Network connect computers to each other, to the internet and to the wired network.
Wi-Fi uses licensed and un-licensed spectrum based on range.
The different Standards are …IEEE 802.11a … IEEE 802.11b and IEEE 802.11g
Primarily, IEEE 802.11b and IEEE 802.11g are being higly used in the market…
As the diagram depcits … wirered network connected to Internet is connected to the wirelss wi-fi world through Access Point which is as if acting like a brings between wirelss and wireline network
…Wi-fi enabled network can access other wi-Fi devices or wireed network devices through this Access Point…

## Slide 223: Elements of a WI-FI Network
Access Point (AP) - A wireless LAN transceiver or “base station” that can connect one or many wireless devices simultaneously to the Internet
Wi-Fi cards - Accept wireless signals & relay information. They can be internal and external. (e.g PCMCIA Card for Laptop and PCI Card for Desktop PC)
Safeguards - Firewalls and anti-virus software protect networks from uninvited users and keep information secure.
Notes: Elements of Wi-Fi network ….
There are primarily three elements of Wi-Fi network …First one amongst them is an access point
Access Point or AP is a wireless LAN transceiver or “base station” that can connect one or many wireless devices simultaneously to the Interne
Second element is a wi-card card …They accept the wireless signal and relay information….They can be internal and external ….e.g PCMCIA Card for Laptop and PCI Card for Desktop PC ….
Then the third element is Safeguards ….Firewalls and anti-virus software protect networks from uninvited users and keep information secure.

## Slide 224: How a Wi-Fi Network Works?
Basic concept is same as Walkie talkies
A Wi-Fi hotspot is created by installing an access point to an internet connection
An access point acts as a base station
When Wi-Fi enabled device encounters a hotspot the device can then connect to that network wirelessly
A single access point can support up to 30 users and can function within a range of 100 – 150 feet indoors and up to 300 feet outdoors
Many access points can be connected to each other via Ethernet cables to create a single large network
Notes: Now let’s try to understand ‘How a Wi-Fi network works’ ?
Basic concept is same as Walkie talkies.
A Wi-Fi hotspot is created by installing an access point to an internet connection.
An access point acts as a base station.
When Wi-Fi enabled device encounters a hotspot the device can then connect to that network wirelessly.
A single access point can support up to 30 users and can function within a range of 100 – 150 feet indoors and up to 300 feet outdoors.
Many access points can be connected to each other via Ethernet cables to create a single large network.

## Slide 225: Wi-Fi Applications
Home
Small Businesses or SOHO
Large Corporations & Campuses
Health Care
Wireless ISP (WISP)
Travellers
Notes: Different Wi-fi applications are mentioned here…
We can use it at home.. Small Businesses or SOHO …Large Corporations & Campuses …Health Care
Wireless ISP (WISP) …Travellers

## Slide 226: Wi-Max
Worldwide Interoperability for Microwave Access
IEEE 802.16 standards-based wireless technology poised to be the next best thing
Aims to provide high-throughput wireless broadband connections over long distances
Fixed last-mile broadband access as a replacement or substitute for wired DSL, cable, or T1/E1 connections
Hotspot subscriber and backhaul provider connections supported
High-speed enterprise connectivity for business
IEEE 802.16-2000, fixed subscriber and provider backhaul standards; racing to production
IEEE 802.16e, mobility for subscribers, finalizing standards; racing to prototypes
Notes: Now we move on to the third wireless access technology called Wi-Max…
Wi max stands for ….Worldwide Interoperability for Microwave Access
It uses IEEE 802.16 standards-based wireless technology poised to be the next best thing
It Aims to provide high-throughput wireless broadband connections over long distances
Fixed last-mile broadband access as a replacement or substitute for wired DSL, cable, or T1/E1 connections
Hotspot subscriber and backhaul provider connections supported
High-speed enterprise connectivity for business
There are two different standards in Wi-max…
IEEE 802.16-2000 …. A standard for fixed subscriber and provider backhaul standards; racing to production
Then IEEE 802.16e, it is for ….mobility for subscribers, finalizing standards; racing to prototypes
These are two broad standards…

## Slide 227: Wi-Max Architecture
Notes: Wi-Max architecture and different components involved in a Wi-Max network…
The core component of Wi-Max system is a subscriber station or othrwise know as CPE I.e Customer Premises Equipment..
In this diagram CPE is shown
Second component is a base station ..Base station and one or more subscriber stations or CPEs can form a cell…with point to multi-point structure…
Base station in this diagram is shown with the green tower present at the center of the diagram…
Apart from this different elements of network are shown over here…like …The network management system or so called NMS which is used to monitor the whole wi-max network…the Local exchange to which Wi-max base station can be connected …
Then 2G/3G gateway to which wi-max network is connected …
And wi-max network is connected to ISP Internet Service Provider through a router which is part of data network like TCP/IP …
So a typical Wi-Max architecture is represented in this diagram…

## Slide 228: Wi-Max Features
Long Range, High Data Rate
Less susceptible to interference
Very viable mobile alternative to DSL and cable
Subscribers receive wireless broadband data delivery to the home
Plug and Play installation
Notes: Let’s have a look at Wi-max Features…
It provides long Range, High Data Rate…the range can be maximum upto maximum of 50 kms in a frequency range of 2 –11 GHz…
And data rate can reach upto 280 megabytes/per second…
Wi-max provides less susceptibility to interference…
Very viable mobile alternative to DSL and cable…
Subscribers receive wireless broadband data delivery to the home
And Plug and Play installation

## Slide 229: Wi-Fi and Wi-Max Comparison
Notes: Here goes a comparison between Wi-Fi and Wi-Max network….
Just read the table…
With this we come towards an end of the module ‘Wireless Access technology – Bluetooth , Wi-fi and Wi-Max’

## Slide 230: Summary
In this session, we have learned:
  Classification IEEE wireless standards along with their range of operations
  Bluetooth network at a very conceptual level
  Wi-Fi andWi-Max network from a perspective of network composition, working and applications
  Comparison of Wi-Fi and Wi-Max network

## Slide 231: Thank You

## Slide 232: Communication Museum

## Slide 233: The Morse Telegraph Samuel Morse, 1791-1872
First electrical telegraph demonstrated in 1837

## Slide 234: Marconi: Wireless Telegraphy
1895 Guglielmo Marconi
q first demonstration of wireless telegraphy (digital!)
q long wave transmission, high transmission power necessary (> 200kw)

## Slide 235: Hertz
H. Hertz (1857-94): demonstrates with an experiment the wave character of electrical transmission through space (1886, in Karlsruhe, Germany, at the location of today’s University of Karlsruhe)

## Slide 236: The Chappe Telegraph (Claude Chappe, 1763-1805)
92 out of
256 (= 4*8*8) positions
represented characters.
Integrity of message could be restored at each relay station
In 1844,
534 relays linked Paris with 29 cities, covering in total 5000 Km.

## Slide 237: Alexander Graham Bell

## Slide 238: The Original Invention
Graham Bell , 1876

## Slide 239: Telephone Instrument Evolution

## Slide 240: Local battery Phone

## Slide 241: Rotary Selector

## Slide 242
Manual Exchange

## Slide 243: Shannon’s Theorem
DataRate <= B.Log2(1+S/N)
B : Channel Bandwidth (in Hertz)
S/N : Signal to Noise ratio
Example:
Telephone channel,
B = 3000 Hz, S/N = 1000
DataRate <= 30 000 b/s

## Slide 244: Fourier
Fourier

## Slide 245: Computer Network: NUTS and BOLTS

## Slide 246: Hubs, Switches, Access Point

## Slide 247: Internet USA structure

## Slide 248: Satellite Communication : Quick Journey

## Slide 249: History of satellite communications
1945: Arthur C. Clarke publishes an essay about „Extra Terrestrial Relays“
1957: first satellite SPUTNIK
1960: first reflecting communication satellite ECHO
1963: first geostationary satellite SYNCOM
1965: first commercial geostationary satellite “Early Bird“
(INTELSAT I): 240 duplex telephone channels or 1 TV channel, 1.5 years lifetime

## Slide 250: History of satellite communications
1976 : three MARISAT satellites for maritime communication
1982: first mobile satellite telephone system INMARSAT-A
1988: first satellite system for mobile phones and data communication INMARSAT-C
1993: first digital satellite telephone system
1998: global satellite systems for small mobile phones

## Slide 251
INTELSAT 806 satellite
Special purpose communication satellites
Ref: INTELSAT

## Slide 252: GPS and Iridium
The Iridium system has 66 satellites in six LEO orbits, each at an altitude of 750 km.
Iridium is designed to provide direct worldwide voice and data communication using handheld terminals, a service similar to cellular telephony but on a global scale.

## Slide 253: TELEDESIC system
Teledesic has 288 satellites in 12 LEO orbits, each at an altitude of 1350 km.

## Slide 254: Comparison of Satellite Network

## Slide 255: A Mobile Station
Front of Circuit board Back of Circuit board

## Slide 256: A Mobile Station
      Circuit board containing the brains of the phone
        Microprocessor
        DSP
        A to D Converter
        D to A Converter
        Memory
      Antenna
      RF & Power sections
      Liquid Crystal Display
      Keyboard
      Microphone
      Speaker

## Slide 257: Present Network Architectures
SONET/SDH
DWDM
ATM
IP
Several distinct, independent control layers

## Slide 258: Thank you